## Slide 1
NTNU - NORWEGIAN UNIVERSITY OF SCIENCE AND TECHNOLOGY
SPECIALIZATION PROJECT 2013-2014
TKP 4550
Supervisor: Krister FORSMAN Co-supervisor: Siguird SKOGESTAD Student: Quang Khoa LE
Azetropic distillation process: Acetic acid dehydration

## Slide 2
Introduction
Thermodynamic model analysis
Process simulation
Results
Analysis on multiple steady states
Contents

## Slide 3
I. Introduction
Acetic acid dehydration: an important step in the production of purified isophthalic acid.
Acetic acid(HAC) – Water system

## Slide 4
Heterogeneous azeotropic distillation
Entrainer: Isobutyl Acetate (IBA)
Changes the relative volatility of the azeotropic constituent
Form a minimum boiling azeotrope water-IBA (88,6°C)
I. Introduction
Difficult to operate : Distillation boundaries, phase split, multicomponent presenting in the column and the possible existence of multiple steady states.

## Slide 5
II. Thermodynamique model analysis
Aspen simulator provides some models that may be used for highly non-ideal chemical system : UNIQUAC, UNIFAC, NRTL (nonrandom two liquids).
Chart: UNIQUAC
| 0 | 0.125 | 0.15 | 0.17499999999999999 | 0.2 | 0.22500000000000001 | 0.25 | 0.27500000000000002 | 0.3 | 0.32500000000000001 | 0.35 | 0.375 | 0.4 | 0.42499999999999999 | 0.45 | 0.47499999999999998 | 0.5 | 0.52500000000000002 | 0.55000000000000004 | 0.57499999999999996 | 0.6 | 0.625 | 0.65 | 0.67500000000000004 | 0.7 | 0.72499999999999998 | 0.75 | 0.77500000000000002 | 0.8 | 0.82499999999999996 | 0.85 | 0.875 | 0.9 | 0.92500000000000004 | 0.95 | 0.97499999999999998 | 1
ASPEN+ | 0 | 0.3009 | 0.3407 | 0.3765 | 0.4089 | 0.4383 | 0.4654 | 0.4903 | 0.5135 | 0.5352 | 0.5555 | 0.5747 | 0.5928 | 0.6101 | 0.6266 | 0.6425 | 0.6577 | 0.6725 | 0.6868 | 0.7008 | 0.7145 | 0.728 | 0.7413 | 0.7545 | 0.7678 | 0.7812 | 0.7948 | 0.8087 | 0.8232 | 0.8383 | 0.8544 | 0.8718 | 0.8909 | 0.9123 | 0.9367 | 0.9654 | 1
experimental data | 0 | 0.3063 | 0.4467 | 0.5973 | 0.658 | 0.7112 | 0.7797 | 0.8239 | 0.8671 | 0.9042 | 0.9186 | 0.9409 | 0.9708 | 1
Chart: NRTL
| 0 | 0.125 | 0.15 | 0.17499999999999999 | 0.2 | 0.22500000000000001 | 0.25 | 0.27500000000000002 | 0.3 | 0.32500000000000001 | 0.35 | 0.375 | 0.4 | 0.42499999999999999 | 0.45 | 0.47499999999999998 | 0.5 | 0.52500000000000002 | 0.55000000000000004 | 0.57499999999999996 | 0.6 | 0.625 | 0.65 | 0.67500000000000004 | 0.7 | 0.72499999999999998 | 0.75 | 0.77500000000000002 | 0.8 | 0.82499999999999996 | 0.85 | 0.875 | 0.9 | 0.92500000000000004 | 0.95 | 0.97499999999999998 | 1
ASPEN+ | 0 | 0.2071 | 0.2438 | 0.2792 | 0.3133 | 0.3461 | 0.3778 | 0.4085 | 0.4381 | 0.4668 | 0.4945 | 0.5214 | 0.5474 | 0.5727 | 0.5972 | 0.621 | 0.6441 | 0.6666 | 0.6884 | 0.7096 | 0.7303 | 0.7505 | 0.7701 | 0.7892 | 0.8078 | 0.826 | 0.8437 | 0.861 | 0.8779 | 0.8944 | 0.9105 | 0.9263 | 0.9417 | 0.9567 | 0.9715 | 0.9859 | 1
experimental data | 0 | 0.3063 | 0.4467 | 0.5973 | 0.658 | 0.7112 | 0.7797 | 0.8239 | 0.8671 | 0.9042 | 0.9186 | 0.9409 | 0.9708 | 1
Chart: UNIFAC
| 0 | 0.125 | 0.15 | 0.17499999999999999 | 0.2 | 0.22500000000000001 | 0.25 | 0.27500000000000002 | 0.3 | 0.32500000000000001 | 0.35 | 0.375 | 0.4 | 0.42499999999999999 | 0.45 | 0.47499999999999998 | 0.5 | 0.52500000000000002 | 0.55000000000000004 | 0.57499999999999996 | 0.6 | 0.625 | 0.65 | 0.67500000000000004 | 0.7 | 0.72499999999999998 | 0.75 | 0.77500000000000002 | 0.8 | 0.82499999999999996 | 0.85 | 0.875 | 0.9 | 0.92500000000000004 | 0.95 | 0.97499999999999998 | 1
ASPEN+ | 0 | 0.3012 | 0.3432 | 0.3813 | 0.4159 | 0.4475 | 0.4765 | 0.5031 | 0.5278 | 0.5506 | 0.5718 | 0.5916 | 0.6101 | 0.6274 | 0.6437 | 0.659 | 0.6736 | 0.6874 | 0.7005 | 0.7131 | 0.7251 | 0.7368 | 0.7482 | 0.7594 | 0.7704 | 0.7815 | 0.7927 | 0.8042 | 0.8163 | 0.8292 | 0.8433 | 0.8591 | 0.8771 | 0.8985 | 0.9245 | 0.9572 | 1
experimental data | 0 | 0.3063 | 0.4467 | 0.5973 | 0.658 | 0.7112 | 0.7797 | 0.8239 | 0.8671 | 0.9042 | 0.9186 | 0.9409 | 0.9708 | 1
=> NRTL

## Slide 6
Vapor phase non ideality caused by the dimerization of Acetic Acid => Hayden-O’connell (HOC)
=> NRTL-HOC
II. Thermodynamique model analysis

## Slide 7
III. Process simulation
Liquid feed stream composition (%):
HAC 73 – 78
Water 20 – 25
MA 1.2 – 1.6
MX 0.02
IBA 0.1 – 0.2
MeOH 0.01
Vapor feed stream composition (%):
HAC 90 – 92
Water 7 – 8.5
MA 0.5 – 0.8
MX negligible
IBA negligible
MeOH negligible
Feed composition
Legend:
HAC: Acetic Acid MX: Metaxylene IBOH: Isobutanol
MA: Methyl Acetate IBA: Isobutyl Acetate MeOH: Methanol

## Slide 8
Flow sheet and product specification
Product Specification:
Top: Bottom:
HAC < 0.1% Water 6 – 7%
IBA < 0.4 %

## Slide 9
IV. Results
Three steady state solutions were obtained.
Only one can satisfy the product specifications with a reasonable energy requirement

## Slide 10
1. Steady state SS1
=> Undesired
L_IBA (IBA ref) (kg/h) | 20000 | 24000
B (bottom kg/h) | 25500 | 25500
Xwater | 0.108995 | 0.09803
X IBA | 3.7E-06 | 2.3E-06
XHAC | 0.891001 | 0.901968
D (top product kg/h) | 5776.977 | 5865.878
Xwater | 0.726584 | 0.767234
XHAC | 0.214185 | 0.180826
Product Specifications:
Bottom: Water 6 – 7%
Top : HAC < 0.1%

## Slide 11
2. Steady state SS2
LIBA(IBA ref) | 20000 | 18000
B (bottom kg/h) | 25500 | 25500
Xwater | 0.0155268 | 0.0274451
X IBA | 0.028294502 | 0.016377263
XHAC | 0.9559729 | 0.9559729
D (top product kg/h) | 6884.22 | 6557.035
Xwater | 0.9688071 | 0.9701339
XHAC | 2.16E-09 | 2.25E-08
=> Undesired
Product Specifications:
Bottom: IBA < 0.4 %

## Slide 12
3. Steady state SS3
=> Desired
LIBA(IBA ref) | 22000 | 19000
B (bottom kg/h) | 25500 | 25500
Xwater (%) | 0.04296 | 0.041327
X IBA (%) | 0.001192 | 0.002708
XHAC (%) | 0.955843 | 0.955936
D (top product kg/h) | 6137.241 | 6179.337
Xwater (%) | 0.971139 | 0.971354
XHAC (%) | 0.000457 | 0.000131
Product Specifications:
Bottom: Water 6 – 7%
IBA < 0.4 %
Top : HAC < 0.1%

## Slide 13
V. Analysis on multiple steady states
Chart: IBA REF
Chart: IBA REF
Figure a: manipulated variable: IBA reflux flow rate
Chart: Water ref ratio
| 0.1 | 0.11 | 0.12 | 0.13 | 0.14000000000000001 | 0.15 | 0.16 | 0.17 | 0.18 | 0.19 | 0.2 | 0.21 | 0.22 | 0.23 | 0.24 | 0.25 | 0.26 | 0.27 | 0.28000000000000003 | 0.28999999999999998 | 0.3 | 0.31 | 0.32 | 0.33 | 0.34 | 0.35
SS1 | 0.88575 | 0.88643 | 0.88713 | 0.88785 | 0.8886 | 0.88938 | 0.89017 | 0.891 | 0.89187 | 0.89276 | 0.89369 | 0.89465 | 0.89565 | 0.89667 | 0.89776 | 0.89885 | 0.90004 | 0.90125 | 0.9025 | 0.90379 | 0.90507 | 0.90632 | 0.90749 | 0.90868 | 0.90987 | 0.91106
SS2 | 0.95597 | 0.95597 | 0.95597 | 0.95597 | 0.95597 | 0.95597 | 0.95597 | 0.95597 | 0.95597 | 0.95597 | 0.95597 | 0.95597 | 0.95597
SS3 | 0.95594 | 0.95593 | 0.95592 | 0.95591 | 0.9559 | 0.95589 | 0.95589 | 0.95588 | 0.95587 | 0.95586 | 0.95585 | 0.95584 | 0.95583 | 0.95582 | 0.95581 | 0.9558 | 0.95579 | 0.95578 | 0.95577 | 0.95576 | 0.95575 | 0.95575 | 0.95574 | 0.95573 | 0.95572 | 0.95572
Chart: Water ref ratio
| 0.1 | 0.11 | 0.12 | 0.13 | 0.14000000000000001 | 0.15 | 0.16 | 0.17 | 0.18 | 0.19 | 0.2 | 0.21 | 0.22 | 0.23 | 0.24 | 0.25 | 0.26 | 0.27 | 0.28000000000000003 | 0.28999999999999998 | 0.3 | 0.31 | 0.32 | 0.33 | 0.34 | 0.35
SS1 | 4.7182 | 4.7539 | 4.7907 | 4.8289 | 4.8683 | 4.9095 | 4.9507 | 4.9946 | 5.0403 | 5.087 | 5.1357 | 5.1863 | 5.239 | 5.2931 | 5.3505 | 5.4079 | 5.4712 | 5.5353 | 5.6024 | 5.6722 | 5.7446 | 5.8207 | 5.8983 | 5.9804 | 6.064 | 6.1508
SS2 | 5.283 | 5.3684 | 5.4541 | 5.5419 | 5.6318 | 5.7238 | 5.8174 | 5.912 | 6.007 | 6.1014 | 6.1928 | 6.2859 | 6.3753
SS3 | 5.3207 | 5.3597 | 5.3999 | 5.4415 | 5.4843 | 5.5284 | 5.5738 | 5.6205 | 5.6686 | 5.7181 | 5.769 | 5.8215 | 5.8754 | 5.9309 | 5.9881 | 6.047 | 6.1077 | 6.1702 | 6.2346 | 6.3009 | 6.3694 | 6.4399 | 6.5127 | 6.5878 | 6.6653 | 6.7452
Figure b: manipulated variable: water reflux ratio

## Slide 14
Thank you for your attention

## Slide 15
The simulation is start up with:
IBA reflux flow rate: 20000 kg/h Bottom flow rate : 26500 kg/h Water reflux ratio : 0.17
The low steady state SS1 is achieved first, then we increase IBA reflux up to 32000 kg/h, we are still at SS1 solution branch.
Increase IBA reflux up to 37000 kg/h, and here we jump to the high steady state SS2. Then IBA reflux is decreased gradually with a step of 2000 kg/h until reach SS3 at about 19000 kg/h.
How to jump from SS1 to SS2 and SS3