## Slide 1: Models for online control of batch polymerization processes.
Student: Fredrik Gjertsen
Supervisor, NTNU: Prof. Sigurd Skogestad
Supervisor, external: Peter Singstad, Cybernetica AS
Background: Summer internship
  Copolymerization reactor model written in the Modelica programming language.
Main goal: Offline parameter estimation
  The established models are mainly made from first principles, and model validation is required in order to verify the model.
  Use experimental data together with the Cybernetica ModelFit software to improve the model.
Ultimate scope: Obtain a high-end model for which an MPC controller can be designed, using online estimation and optimization. Controller design is left for masters thesis.

## Slide 2: The copolymerization model
Two-phase emulsion copolymerization of styrene and butyl acrylate
Quite comprehensive model
  ~ 30 states
  ~ 35 parameters
Considerations with respect to computational time must be done
  Implementation in a control system

## Slide 3: Progress
Learn to use software for parameter estimation
  Theory of estimation
Acquire experimental data from one or more reactors (labscale or industrial scale).
Perform off-line parameter fitting
  Kinetic adjustment factors
  Heat transfer properties