## Slide 1: ADVANCED PROCESS CONTROL
Sigurd Skogestad
Department of Chemical Engineering
Norwegian University of Science and Technology (NTNU)
Trondheim
CNCA2021, 13 October 2021, Mexico (virtual)

## Slide 2: Abstract
Title: Advanced process control.
Control engineers rely on many tools, and although some people may think that in the future there will be one general universal tool that solves all problems, like model predictive control, this is not likely to happen. The main reason is that the possible benefits of using more general tools may not be worth the increased implementation costs (including modelling efforts) compared to using simpler "conventional" advanced process control (APC) solutions. In particular, this applies to process control, where each process is often unique. In addition, for a new process, a model is usually not available, so at least for the initial period of operation a conventional scheme must be implemented.
Conventional APC, includes the “advanced” standard control elements that typically are provided at the DCS (distributed control system) level and which industry commonly uses to enhance control when simple single-loop PID controllers do not give acceptable control performance. Examples of such control elements are cascade control, selectors (override), split range control, input or valve position control (VPC), multiple controllers (and MVs) for the same CV, and nonlinear calculation blocks (including nonlinear feedforward and decoupling and linearizing adaptive gain elements).
Since its introduction in the 1940’s, about 80 years ago, conventional APC has largely been overlooked by the academic community, yet it is still thriving in industrial practice, even after 40 years with MPC. So it seems safe to predict that conventional APC (including PID control) will not be replaced by MPC, but will remain in the toolbox along with MPC. The goal of this talk is to take a systematic view on how to design a conventional APC system. The starting point is the plantwide optimal steady-state economic operation, with focus on constraints.
Some more details (not send to conference):
Since conventional APC it is not going away any time soon, it is definitely time to strengthen its theoretical basis and train students on how to use it in an effective manner.
The goal of this talk is to take a systematic view on how to design a conventional APC system. The starting point is to consider the plantwide optimal steady-state economic operation, with focus on constraints. The next issue to consider is inventory control, where the concept of throughput manipulator (TPM) is central as it determines the structure of the inventory control system. Following this, one needs to consider how active constraint switching can be implemented and this leads to selectors (for CV switching) and split range control, multiple controllers or VPC (for MV switching). Other issues are disturbances and nonlinearity, where cascade control and calculation blocks may be helpful.
The main disadvantage with conventional APC compared to MPC is that it is based on single-loop controllers, so one needs to pair outputs (CVs) with inputs (MVs). For most processes this works well, but for more complex cases with many constraint switches one may get significant benefits and simplifications with MPC. Other cases where MPC may offer significant benefits compared to conventional APC is for interactive processes and for cases with known future disturbances.

## Slide 3
Trondheim
Arctic circle
Geiranger fjord
Trondheim

## Slide 4: About Sigurd Skogestad
•1955: Born in Norway
•1978: MS (Siv.ing.) in chemical engineering at NTNU
•1979-1983: Worked at Norsk Hydro co. (process simulation)
•1987: PhD from Caltech (supervisor: Manfred Morari)
•1987-present: Professor of chemical engineering at NTNU
• 1994-95: Visiting Professor UC Berkeley
• 2001-02: Visiting Professor UC Santa Barbara
•1999-2009: Head of ChE Department, NTNU
•2015-..: Director SUBPRO (Subsea research center at NTNU)
Non-professional interests:
mountain skiing (cross country)
orienteering (running around with a map)
grouse hunting

## Slide 5: “The goal of my research is to develop simple yet rigorous methods to solve problems of engineering significance”
One example: SIMC PID tuning rules (Skogestad, JPC, 2003)
«Probably the best simple PID tuning rules in the world»

## Slide 6: Outline
Optimization and control
  Control hierarchy
  Want tight control of constraints
    Lagrange multipliers
    Selectors
Classical advanced (process) control (APC)
  Selectors
  Feedforward, decoupling and linearization blocks
    Input transformations (Feedback linearization)
  Other elements
    Split range control, valve position control, cascade
Conclusion. MPC vs. classical APC

## Slide 7: Main notation Control: Given setpoints
Controller
Process
Input
u=MV
Disturbance
d=DV
Setpoint
ys =CVs
Output
y=CV
Feedback
Feedforward
MV = Manipulated Variable
CV = Controlled Variable
This talk: Focus on feedback

## Slide 8: Process control: Hierarchical decision system
CV2s
CV1s
Manager
Process engineer
Operator/RTO (usually steady-state)
Supervisory control layer
”Advanced control”/MPC
PID-control
u (MV) = valves
min J (economics)
hour
Setpoint control
(+ look after other variables)
minute
Stabilize + avoid drift
second

## Slide 9: Process control: Hierarchical decision system
Manager
Process engineer
min J (economics)
hour
Setpoint control
(+ look after other variables)
minute
Stabilize + avoid drift
second
Economic MPC
(EMPC)
or
Dynamic RTO
u (MV) = valves

## Slide 10: Process control: Hierarchical decision system
Manager
Process engineer
min J (economics)
hour
Setpoint control
(+ look after other variables)
minute
Stabilize + avoid drift
second
Economic MPC
(EMPC)
or
Dynamic RTO
u (MV) = valves
CV2s

## Slide 11: Process control: Hierarchical decision system
Manager
Process engineer
Operator/RTO (usually steady-state)
Supervisory control layer
”Advanced control”/MPC
PID-control
u = valves
min J (economics)
hour
Setpoint control
(+ look after other variables)
minute
Stabilize + avoid drift
second
Focus of this talk
CV1s

## Slide 12: How do we design the control system for a large process?
Consider economics
  minu J(u,d) s.t. g(u,d)≥0
Translate into control: Find good controlled variables (CV1) to keep at fixed setpoints
CV1 = Active constraints (can change!)
CV1 = «Self-optimizing» variables (related to gradient y = Ju = 0)
2. Design control system to control CV1 under varying conditions (disturbances)
Usually two control layers:
Supervisory control layer («advanced control»), CV1
Stabilizing control layer («PID control»), CV2

## Slide 13: «ADVANCED/SUPERVISORY CONTROL» LAYER
Objectives :
1. Control primary variables CV1 at setpoints computed by RTO
    Tight control of active constraints is often desired for economic reasons.
  Feedforward from measured disturbances
    If helpful
  Make use of extra inputs
  Make use of extra measurements
2. Switch control structures (CV1) depending on operating region
  Change in active constraints
  Identify “self-optimizing variables”
  3. Keep an eye on stabilizing layer
    Avoid saturation in stabilizing layer, may require switching
Implementation:
Alternative 1: Advanced control based on ”simple elements” (decentralized control)
Alternative 2: MPC

## Slide 14: Academia: MPC
MPC
    General approch, but we need a dynamic model
    MPC is usually implemented after some time of operation
    Not all problems are easily formulated using MPC
    Explicit control of changing active constraints requires additional logic
      Industry uses two-stage MPC with steady-state feasibility based on constraint priority list

## Slide 15: Research question: Alternative simpler solutions to MPC
Would like: Feedback solutions that can be implemented without a detailed models
Machine learning?
  Requires a lot of data
  Can only be implemented after the process has been in operation
But we have "classical advanced control“ based on single-loop PIDs
  Extensively used by industry
  Problem for engineers: Lack of design methods
    Has been around since 1940’s
    But almost completely neglected by academic researchers
  Main fundamental limitation: Based on single-loop (need to choose pairing)

## Slide 16: “Classical Advanced control” using simple control elements
Cascade controllers
Have Extra output (state) measurements
2. Feedforward elements
Have measured disturbance
3. Decoupling elements
Have interactive process
4. Linearization elements / Adaptive gain
Have Nonlinear process
5. Split-range control (or multiple controllers or VPC)
Need extra inputs (MV) to handle all conditions (steady state) (MV-MV switch)
6. Valve position control (VPC) (Input resetting/Midranging control)
Have extra inputs dynamically
7. Selectors
Have changes in active constraints (CV-CV switch)
APC: Often static nonlinear «function block»
One unifying approach is «Transformed inputs» (similar to feedback linearization)

## Slide 17: How design classical APC elements?
Industrial literature (e.g., Shinskey).
Many nice ideas. But not systematic. Difficult to understand reasoning
Academia: Very little work

## Slide 18: 7. Change in CVs (active constraints) using selectors

## Slide 19: Want tight control of constraints for economic reasons
minu J(u,d)
s.t. g(u,d) ≥ 0
Active constraint: gA=0
Tight control of gA minimizes «back-off»
How can we identify and control active constraints?
Example. Drive from a to B in shortest time
J = T
u = power (gas pedal)
g1 = speed limit = vmax - v
g2 = safety limits
Straight road:
gA = g1 (Speed limit)
A
B

## Slide 20: Feedback solution that automatically tracks active constraints by adjusting Lagrange multipliers (= shadow prices = dual variables) λ
«Optimal Resource Allocation using Distributed Feedback-based Real-time Optimization». Risvan Dirza, Sigurd Skogestad, Dinesh Krishnamoorthy. IFAC Adchem Conference, 2021
Process
Unconstrained optimization
(nu PID-controllers)
Gradient estimation
Constraint control
(nc slower PI/I-controllers)
MAX
0
y
g (measured constraint)
g (measured constraint)
SP=0
SP=0
u
d
Primal-dual feedback control.
Makes use of «dual decomposition» of constrained optimization
Selector on dual variables λ
Problem: Constraint control using dual variables is on slow time scale
Dual variables
Primal variables

## Slide 21: Alternative: Feedback solution with «direct» constraint control
Process
Gradient estimation
Constraint controllers
(fast PID-controllers)
MAX/
MIN
y
g (measured constraint)
g (constraints paired with u1)
SP=0
u1
d
u2
Ju1
u1
(changes!)
Ju2
PID
u1o
SP=0
Ju1, Ju2 = NTJu reduced gradients
(«self-optimizing variables»)
«Online Process Optimization with Active Constraint Set Changes using Simple Control Structure», D. Krishnamoorthy and S. Skogestad, I&EC Res., 2019
«Optimal controlled variables for ̈ polynomial systems». Jaschke, J.; Skogestad, S., J. Process Control, 2012
Selector on primal variables (inputs)
Similar to selectors in APC

## Slide 22: Selector (APC): One input (u), several outputs (y1,y2)
Sometimes called “override”
Selectors are used for output-output (CV-CV) switching
  Example: Normally want to keep y1 at a setpoint,
    but y2 (higher priority) must not exceed constraint.
    With selector: When y2 reaches constraint, we give up control of y1.
    More generally: u1=uo is the optimal input value without constraint (can be given up)
  Can have many constraints paired with same input y.
Selectors work well, but require pairing each constraint with a given input (not always possible)
>
MAX
=
HS
=
<
MIN
=
LS
=
y1
y2
u=min(u1,u2)

## Slide 23: Design of selector structure
Rule 1 (max or min selector)
Use max-selector for constraints that are satisfied with a large input
Use min-selector for constraints that are satisfied with a small input
Rule 2 (order of max and min selectors):
If need both max and min selector: Potential infeasibility
Order does not matter if problem is feasible
If infeasible: Put highest priority constraint at the end
“Systematic design of active constraint switching using selectors.”
Dinesh Krishnamoorthy , Sigurd Skogestad. Computers & Chemical Engineering, Volume 143, (2020)

## Slide 24: Example A. Maximize flow with pressure constraints
Op
Input u = z1
Want to maximize flow, J=-F:
Unconstrained: Optimal input is infinity:

## Slide 25
Desired input u0 without constraints (can be given up) into first selector block
Disturbances in p0 and p2 (unmeasured)

## Slide 26
t>1800: u=zmax=1

## Slide 27
Example B. Maximize production
for serial process
Constraints on levels (H,L)
and valves/flows
TPM = throughput manipulator
Typically at bottleneck («active constraint»)
Disturbances: Temporary bottelenecks
(max-constraints) for F0, F1, F2 or F3

## Slide 28
Example B. Very smart selector strategy: Bidirectional inventory control
Reconfigures automatically with optimal buffer management!!
F.G. Shinskey, «Controlling multivariable processes», ISA, 1981
C. Zotica, S. Skogestad and K. Forsman, Comp. Chem. Eng, 2021
Max flow:
Fs=∞

## Slide 29
F0=1
F2=1
F3=1
F1=1
1
=∞
=∞
=∞

## Slide 30
F0=1
F2=1
F3=1
F1=0.5
1
=∞
=∞
0.5

## Slide 31
F0=0.5
F2=1
F3=1
F1=0.5
1
0.5
=∞
=∞

## Slide 32
F0=0.5
F2=0.5
F3=1
F1=0.5
1
0.5
=∞
=∞

## Slide 33
F0=0.5
F2=0.5
F3=0.5
F1=0.5
1
0.5
=∞
=∞
=∞

## Slide 34
F0=1
F2=1
F3=1
F1=1
1
=∞
=∞
Challenge: Can MPC be made to do his? Optimally reconfigure loops and find optimal buffer? I doubt it. We tried.

## Slide 35: Important insight
Many problems: Optimal steady-state solution always at constraints
In this case optimization layer may not be needed
  if we can identify the active constraints and control them using selectors (Examples A and B).

## Slide 36: Anti-windup
All the controllers shown need anti-windup to «stop integration» during periods when the control action (vi) is not affecting the process:
  Controller is disconnected (because of selector)
  Physical MV ui is saturated
Anti-windup using back-calculation. Typical choice for tracking constant, KT=1
KT,i
Selector or
saturation

## Slide 37: Challenges selector design
Standard approach requires pairing of each active constraint with a single input
  May not be possible in complex cases
Stability analysis of switched systems is still an open problem
  Undesired switching may be avoided in many ways:
    Filtering of measurement
    Tuning of anti-windup scheme
    Minimum time between switching
    Minimum input change

## Slide 38: “Classical Advanced control” using simple control elements
Cascade controllers
Have Extra output (state) measurements (similar to state feedback)
2. Feedforward elements
Have measured disturbance
3. Decoupling elements
Have interactive process
4. Linearization elements / Adaptive gain
Have Nonlinear process
5. Split-range control (or multiple controllers or VPC)
Need extra inputs (MV) to handle all conditions (steady state) (MV-MV switch)
6. Valve position control (VPC) (Input resetting/Midranging control)
Have extra inputs dynamically
7. Selectors
Have changes in active constraints (CV-CV switch)
APC: Often static nonlinear «function block»
One unifying approach is «Transformed inputs» (similar to feedback linearization)

## Slide 39: 1. Cascade control
Use extra measurement y2 to improve control of primary output y1
Cascade: MV for outer primary controller is the setpoint r2 to inner secondary controller
Fast inner loop: Eliminate d2 and nonlinearity in G2
        Proof: Ideally y2 = r2
Design: First design fast inner/secondary controller (can be just P-control)
Then design slower outer/primary controller (PI-controller)
Closed-loop time constant for outer loop at least 4 times larger (slower)
An alternative approach that uses extra measurements to improve control is «Full state feedback».
Primary
Secondary loop (fast)

## Slide 40: 2,3,4. Feedforward, Decoupling, Linearization
Unified approach (for static case): «Transformed» inputs v (and outputs)*
Greg Shinskey (1981): “There is no need to be limited to single measurable or manipulable variables. If a more meaningful variable happens to be a mathematical combination of two or more measurable or manipulable variables, there is no reason why it cannot be used.”
Motivation: ratio control
*«Transformed Manipulated Variables for Linearization, Decoupling and Perfect Disturbance Rejection»,
C Zotica, N Alsop, S Skogestad, IFAC World Congress, 2020

## Slide 41
Concentrate
q1 [m3/s]
C1 [mol/m3]
q [m3/s]
c [mol/m3]
c
∞
H
Diluted product
LC
C2 small
(Water)
FC
x
(q2/q1)s
q2,s
q1,m
q2,m
CC
cm
cs
RATIO CONTROL
with outer cascade (to adjust ratio setpoint)
MOTIVATING EXAMPLE 1: MIXING PROCESS
Input u=q2.
Transformed input v = q2/q1
Gives “perfect” feedforward control for d=q1
Potential problem for outer feedback loop (composition controller, y=c):
  Gain from MV = (q2/q1)s to CV=c will vary because of multiplication with q1,m
  Outer loop must handle disturbances in c1 and c2

## Slide 42
Concentrate
q1 [m3/s]
C1 [mol/m3]
q [m3/s]
c [mol/m3]
c
∞
H
LC
C2
Water
FC
v
q2,s
q1,m
C1,m
q2,m
CC
cm
cs
Improved RATIO CONTROL = Ideal TRANSFORMED INPUT from static model
Nonlinear Function block
Transformed input v = Right-Hand-Side of static model for y=c:
  c = (q1 c1 + q2 c2)/(q1+q2)
  Solve with respect to input q2.
  Get “nonlinear function block”: q2 = q1*(c1-v)/(v –c2)
Gives “perfect” feedforward control for disturbances in q1, c1 and c2.
and also gives linear response (y=v) for controller CC
=v

## Slide 43: Dynamic case (~ feedback linearization, Isidori)
Nonlinear dynamic system (process)
Introduce transformed inputs
New transformed system is linear, first-order, decoupled if A is diagonal and independent of disturbances!
Static input calculation (inverse input transformation): u is solution to:
v can be set by conventional linear controller C (PI)
  Ideally: Don’t need to change v, but in practice need C to handle uncertainty
Assumptions
  Measure all disturbances (d)
  Low-order model with no. states (y) = no. inputs (u)
  The solution to the static inverse problem exists and satisfies certain properties.

## Slide 44: Example 2. Mix hot (1) and cold (2) water, y=[q T]
Mass balance: (static equation for y1=q)
Energy balance: (dynamic equation for dy2/dt)
New transformed inputs: v0 and v.
Inverse transformation (with u1=q1 and u2=q2):
Tuning parameter, A = -(q/V)* (nominal)
Assume V constant
Mixer

## Slide 45: Resulting Transformed system y1=q, y2=T
Transformed system
Linear, decoupled and independent of disturbances

## Slide 46: Simulation responses with transformation only. -> Perfect disturbance rejection and decoupling
1. d1=T1: 20 ->22 °C at t = 50 s
2. d2=T2: 50 ->55 °C at t = 100 s
3. y2s=Ts: 35 ->36 °C at t = 150 s
4. y1s=qs: 10 ->11 kg/s at t = 200 s
y1
y2
u
d
1,2: v0 and v constant
3: Step in v
4: step in v0

## Slide 47: Use of extra MV (inputs): One CV, many MVs
Two different cases:
5. MV-MV switching: Need several MVs to cover whole range at steady state
  We want to use one MV at a time
6. Have extra dynamic MV
  Both MVs are used all the time

## Slide 48: 5. Extra inputs (MV) to handle all conditions (steady state)
1. Split-range control
Alternatives to Split-range control*:
  2. Multiple controllers with different setpoints
  3. Valve position control
* A. Reyes-Lua and S. Skogestad, «Systematic design of active constraint switching using classical advanced control structures», Ind.Eng.Chem.Res, Vol. 59, 2229-2241 (2020)

## Slide 49
MVs (two for summer and two for winter):
AC (expensive cooling)
CW (cooling water, cheap)
HW (hot water, quite cheap)
Electric heat, EH (expensive)
y=T
Alt. 1 Split-range control (SRC).
Note: may adjust the location of split (x-axis) to make loop gains equal.
Disadvantage SRC: 1. Must use same integral time for all MVs
2. Does not work well for cases where constraint values change
Example: Room heating with one CV (T) and 4 MVs
= 22oC

## Slide 50
MVs (two for summer and two for winter):
AC (expensive cooling)
CW (cooling water, cheap)
HW (hot water, quite cheap)
Electric heat, EH (expensive)
y=T
Alt. 2. Multiple controllers with different setpoints
Example: Room heating with one CV (T) and 4 MVs
C1
C2
C3
C4
23oC
22oC
21oC
20oC

## Slide 51
MVs (two for summer and two for winter):
AC (expensive cooling)
CW (cooling water, cheap)
HW (hot water, quite cheap)
Electric heat, EH (expensive)
y=T
Alt. 3. Input resetting (VPC)
Example: Room heating with one CV (T) and 4 MVs
C1
C2
C3
C4
22oC
10%
10%
10%

## Slide 52: Summary MV-MV switching
Use Alt.1 (split range control) for cases where the MV ranges (max and min values) are fixed.
  Advantage: Easy to understand, because SR-block shows clearly sequence of MVs
Use Alt. 2 (controllers for different setpoints) for cases where MV ranges vary
  Advantage: Easier to implement than SRC and can have different controller tunings
Use Alt. 3 (input resetting) for cases where CV (y) should always be controlled by same MV
  But gives some economic loss

## Slide 53: 6. Extra inputs (MVs) dynamically: Valve position control (VPC)
This VPC is active all the time with the aim «resetting» or «midranging» the input.

## Slide 54
qB
Thot
TC
EXAMPLE. Use of bypass (extra input) for fast control
closed
FC
qBs
TC: Fast control of CV=Thot using the “dynamic” MV2=qB
FC: Resets MV2=qB to its setpoint (qbs) (e.g. 5%) using MV1=CW

## Slide 55: When use MPC?
When conventional APC performs poorly or becomes complex
Cases with many changing constraints (where we cannot assign one input to each constraint)
Interactive process
Know future disturbances and setpoint changes (predictive capability)

## Slide 56: Conclusion Advanced process control
Conventional APC works very well in may cases
  Optimization by feedback (active constraint switching)
  Need to pair input and output.
    Advantage: The engineer can specify directly the solution
    Problem: Unique pairing may not be possible for complex cases
  Need model only for parts of the process (for tuning)
  Challenge: Need better teaching and design methods
MPC may be better (and simpler) for more complex multivariable cases
  But MPC may not work on all problems (Bidirectional inventorycontrol)
  Main challenge: Need dynamic model for whole process
  Other challenge: Tuning may be difficult

## Slide 57
Optimal centralized
Solution (EMPC)
Sigurd (me)
Academic process control community fish pond
Simple solutions that
work (selector, PID++)

## Slide 59: Extra

## Slide 60: Alt. 2. Several controllers with different setpoints
Example
CV=y= room temperature
MV1 = u1 = cooling
CVspH = 22°C (summer)
MV2 = u2 = heating
CVspL = 20 - 2 = 20°C (winter)
Between 20°C and 22°C:
Temperature drifts with both inputs saturated:
    heating off, u1=0
    cooling off, u2=0
Need different setpoints to
Avoid using cooling and heating at the same time
avoid fighting between controllers
Note: The order of when to use each MV is determined by the setpoints. This also works if we have to two or more MVs with the same sign, for example, if we have two heating sources: hot water (as shown in figure) and more expensive electric heat. Then we could add a temperature controller for the electic heat with an even lower setpoint, for example, Ts=18C.

## Slide 61: Alt. 3. Input (valve) position control (VPC)
Keep the original loop (u1-y)
Use u2 to avoid saturation of u1 (VPC)
Advantage: Always use u1 for control of y
Disadvantages: Always use u1 (cannot put at constraint -> economic loss)
Important: Loop C2 with u2 is not active all the time, only when u1 is close to saturation

## Slide 62: Example MV-MV switching: Pressure control
INERT
z2
z3
z3
z2
z3
=0.9 bar
=1 bar
=1.1 bar
=1 bar
z1
z2
z3
CV=p
MV1=heat (Q)
MV2=inert
MV3=vent
Normally: Control CV=p using MV1=Q
but if Q=0 we must use MV3=vent
and if Q=max we must use MV2=inert
Alt.3: VPC
Always use Q (z1) to control p.
Need two VPC’s:
Use vent (z3) to avoid Q=0
Use inert (z2) to avoid Q=max