## Slide 1: Putting optimization into the control layer using the magic of feedback control
Sigurd Skogestad
Department of Chemical Engineering
Norwegian University of Science and Technology (NTNU)
Trondheim
ESCAPE’32. Toulouse, 13 June 2022
Thanks to: Adriana Reyes-Lúa, Cristina Zotică, Dinesh Krishnamoorthy

## Slide 2
Trondheim
Arctic circle
Geiranger fjord
Trondheim

## Slide 3: About Sigurd Skogestad
•1955: Born in Flekkefjord, Norway
• 1956-1961: Lived in South Africa
•1974-1978: MS (Siv.ing.) studies in chemical engineering at NTNU
•1979-1983: Worked at Norsk Hydro co. (process simulation)
•1983-1987: PhD student at Caltech (supervisor: Manfred Morari)
•1987-present: Professor of chemical engineering at NTNU
• 1994-95: Visiting Professor UC Berkeley
• 2001-02: Visiting Professor UC Santa Barbara
•1999-2009: Head of ChE Department, NTNU
•2015-..: Director SUBPRO (Subsea research center at NTNU)
Non-professional interests:
mountain skiing (cross country)
orienteering (running around with a map)
grouse hunting
1973

## Slide 4: “The goal of my research is to develop simple yet rigorous methods to solve problems of engineering significance”

## Slide 5: Outline
Introduction: Optimal economic operation of process plants
Control: Implementing optimal operation in practice
  Model predictive control (MPC)
  Conventional advanced Process control (APC)
Unconstrained Optimization: Self-optimizing variables
Constrained Optimization: Using conventional APC to handle changing active constraints
  Many examples
  PID-control, Selectors, Split range control
Systematic procedure for designing APC
  More Examples
Conclusion

## Slide 6: Optimal economic operation
Minimize cost J = J(u,x,d)
Or: Maximize profit P=-J
u = degrees of freedom
x = states (internal variables)
d = disturbances
J = cost feed + cost energy – value of products
J
uopt
Jopt
u

## Slide 7: Optimal economic operation
Minimize cost J = J(u,x,d)
Subject to satisfying constraints
u = degrees of freedom
x = states (internal variables)
d = disturbances
J
uopt
Jopt
constraint
J = cost feed + cost energy – value of products
u

## Slide 8: Active constraints
Active constraints:
  variables that should optimally be kept at their limiting value.
Active constraint region:
  region in the disturbance space with fixed active constraints
Region 1
Region 2
Region 3
Disturbance 1
Disturbance 2
Optimal operation:
How switch between regions?

## Slide 9: Control is about implementing optimal operation in practice
Many cases: Solution is fully constrained, but constraints change
Key is to control the active constraints
In practice: Don’t need to know regions
if we can measure and control the constraints
Region 1
Region 2
Region 3
Disturbance 1
Disturbance 2

## Slide 10: 2. Control hierarchy in a process plant
Key idea: Time scale separation
Optimization layer (RTO) (hour)
  Minimize economic cost J, satisfying constraints
Supervisory layer (APC or MPC) (minutes)
  Follow set points (CV1) from optimization layer
  Switch between active constraints (CV1 change)
  Look after regulatory layer
Regulatory control (PID) (seconds)
  Follow setpoints (CV2) from layers above
  Stabilize: Control drifting variables
Key decisions: Select CV1 and CV2
CV = Controlled variable
MV = Manipulated variable (process input)
RTO = Real-time optimization
APC = Conventional Advanced process control
MPC = Model predictive control
PID = Propertional-Integral-Derivative
MV

## Slide 11: Optimal operation of process plants
Most people think
  You need a detailed nonlinear model and an on-line optimizer (RTO) if you want to optimize the process
  You need a dynamic model and model predictive control (MPC) if you want to handle constraints
  The alternative is Machine Learning
No! In many cases you just need to measure the constraints and use PID control
  «Coventional advanced process control (APC)»
How can this be possible?
  Because optimal operation is usually at constraints
  PID-controllers can be used to identify and control the active constraints
  For unconstrained degrees of freedom, one often have «self-optimizing» variables
This fact is not well known, even to control professors
  Because most APC-applications are ad hoc
  Few systematic design methods exists

## Slide 12: Example: Optimal operation of runner
  Cost to be minimized, J=T
  One degree of freedom (u=power)
  What should we control?
Sigurd Skogestad. «Near-optimal operation by self-optimizing control: From process control to marathon running and business systems», Comp.Chem.Engng. (2004)

## Slide 13: A. Optimal operation of Sprinter
  100m. J=T
  Active constraint control:
    Run as fast as you can (”no thinking required”)
    CV = power (at max)
Constrained optimum: Control active constraints

## Slide 14: B. Optimal operation of Marathon runner
    40 km. J=T
    What should we control? CV=?
    Unconstrained optimum
u=power
J=T
uopt
Unconstrained optimum: Not obvious what to control

## Slide 15
Any self-optimizing variable (to control at constant setpoint)?
    c1 = distance to leader of race
    c2 = speed
    c3 = heart rate
    c4 = level of lactate in muscles
Marathon runner (40 km)
Unconstrained optimum: Control self-optimizing variables

## Slide 16: Conclusion Marathon runner
CV1 = heart rate
select one measurement
CV = heart rate is good “self-optimizing” variable
Simple and robust implementation
Disturbances (d) are indirectly handled by keeping a constant heart rate
May have infrequent adjustment of setpoint (cs)
c=heart rate
J=T
copt
Control self-optimizing variables

## Slide 17: 3. Unconstrained optimization
Have unconstrained degree of freedom (u)
Available measurements: y
What should we control (c=CV1=Hy)?
  Not at all obvious
u
J
uopt

## Slide 18
Self-optimizing control
Self-optimizing control is when we can achieve an acceptable economic loss (between re-optimizations) with constant setpoint values for the controlled variables (c=CV1)
Self-optimizing control is an old idea (Morari et al., 1980):
“We want to find a function c of the process variables which when held constant, leads automatically to the optimal adjustments of the manipulated variables, and with it, the optimal operating conditions.”
S. Skogestad ``Plantwide control: the search for the self-optimizing control structure'', J. Proc. Control, 2000.

## Slide 19: The ideal “self-optimizing” variable is the gradient, Ju
c =  J/ u = Ju
  Keep gradient at zero for all disturbances (c = Ju=0)
u
cost J
Ju=0
Ju<0
Ju<0
uopt
Ju
0
Problem: Usually no measurement of gradient
Notes: 19

## Slide 20
H
Ideal: c = Ju
In practise, use available measurements: c = H y. Task: Select H!

## Slide 21: Self-optimizing variables: Model-based methods for c=Hy Nullspace method for H HF=0 where F=dyopt/dd
Proof: Want copt independent of disturbance d
Have. yopt = F d, so copt = H yopt = HF d -> HF=0
V. Alstad and S. Skogestad, ``Null Space Method for Selecting Optimal Measurement Combinations as Controlled Variables'', Ind.Eng.Chem.Res, 46 (3), 846-853 (2007)
Exact local method for H
V. Alstad, S. Skogestad and E.S. Hori, ``Optimal measurement combinations as controlled variables'', Journal of Process Control, Vol.19, 128-148 (2009).

## Slide 22: Example. Nullspace Method for Marathon runner
u = power, d = slope [degrees], J=Time
y1 = hr [beat/min], y2 = v [m/s]
c = Hy = h1 y1+ h2 y2
From model or data: F = dyopt/dd = [0.25 -0.2]’
HF = 0 -> h1 f1 + h2 f2 = 0.25 h1 – 0.2 h2 = 0
Choose h1 = 1 -> h2 = 0.25/0.2 = 1.25
Conclusion: c = hr + 1.25 v
Control c = constant -> hr increases when v decreases (OK uphill!)

## Slide 23: Self-optimizing variables: What should we control?
BAD
Good
Good
Engineering insight may be used if we don’t have model
The optimal value of c should be insensitive to disturbances
  Small Fc = HF = dcopt/dd
The value of c should be sensitive to the inputs (“maximum gain rule”)
  Large gain, Gc = HGy = dc/du
  Equivalent: Want flat optimum
I.J. Halvorsen, S. Skogestad, J.C. Morud and V. Alstad, ``Optimal selection of controlled variables'', Ind. Eng. Chem. Res., 42 (14), 3273-3284 (2003)
NEVER try to control a variable that reaches max or min at the optimum
  In particular, never try to control directly the cost J

## Slide 24: Example: Maximize growth of salmon fish (RAS)
One unconstrained degree of freedom: Buffer/base addition
What should we control?
Self-optimizing variable (CV1): pH in Fish tank
  Large gain (sensitive to changes in buffer/base)
  Small variations in optimal setpoint (7-7.5)
  Optimize with simple pH-controller
Allyne M. dos Santos et al., Soft sensor of key components in recirculation aquaculture systems, using feedforward networks, ESCAPE-32 Toulouse, 2022 (Poster today)
pHC
pHC
Regulatory layer: pH-control also provides stabilization
so we have CV2=CV!=pH, which is ideal

## Slide 25: 4. Constrained optimization
Obvious what we should control: Active constraints
  Can be measured in most cases and controlled with PID-controller
Reason for change in active constraints are
  Disturbances (including changes in parameters and prices)
Challenge control: Switch between active constraints
J
uopt
Jopt
constraint

## Slide 26: Conventional advanced control structures (ACS)
Used when single-loop PID is not sufficient.
Examples:
  Cascade control
  Feedforward control / Ratio control
  Decoupling
  Selectors
  Split range control (SRC)
  Input resetting or valve positioning control (VPC)
Can handle constraint changes

## Slide 27: Conventional APC for changing active constraints
Four cases:
  MV-MV switching -> Split Range Control + 2 more options
  CV-CV switching -> Selectors
  Simple CV-MV switching -> Do nothing
  Complex CV-MV switching
MV = Manipulated Variable = Input (u)
CV = Controlled Variable = Output (y)
DV = Disturbance Variable (d)
Process
MV
CV
DV
Adriana Reyes-Lua and Sigurd Skogestad, Systematic Design of Active Constraint Switching Using Classical Advanced Control Structures, Ind.Eng.Chem.Res, 2020

## Slide 28: Optimization with PI-controller
Example: Minimize heating cost (Norway)
min u
s.t. y ≥ ymin
u ≥ umin = 0
(u=heating, y=temperature, ymin=22 °C)
Disturbance (d): Outdoor temperature
Optimal solution has two active constraint regions:
  CV=y = ymin  minimum temperature (winter)
  MV=u = umin  heating off (summer)
  No unconstrained region
Solved with PI-controller («thermostat»)
  ysp = ymin
ysp = ymin
PI
This is simple CV-MV switching
u = input = manipulated variable (MV)
y = output = controlled variable (CV)
We satisfy the input saturation rule:
«When the MV (u) saturates (at 0), control of the CV (y) can be given up»

## Slide 29
MVs:
AC (expensive cooling)
CW (cooling water; cheap)
HW (hot water, quite cheap)
Electric heat, EH (expensive)
y=T
Temeperature control with 4 inputs (MVs)
d=Tamb
CPI – same controller for all inputs (one integral time)
But get different gains by adjusting slopes α in SR-block
This is MV-MV switching
Objective: Minimize cost
Use cheap MVs first and use only one MV at the time (difficult with MPC)
Solution: Split range control (SRC):

## Slide 30
Split-range control (SRC): Simulation of disturbances in ambient temperature.
MPC: Similar output responses (y), BUT different inputs (u). Uses both heating and cooling in some cases
MPC: Needs dynamic model + more difficult to implement and tune
y(t), d(t)
u(t)
A. Reyes-Lúa and S. Skogestad. “Multi-input single-output control for extending the operating range: Generalized split range control using the baton strategy”. Journal of Process Control 91 (2020)
This is MV-MV switching

## Slide 31: Optimization with PI-controller
Example: Drive as fast as possible to airport with small car
max y
s.t. y ≤ ymax
u ≤ umax
(u=power, y=speed)
Disturbance (d): Slope of road
Optimal solution has two active constraint regions:
  CV=y = ymax = 120 km/h  speed limit
  MV=u = umax  max power (steep hill)
Solved with PI-controller («cruise controller»)
  ysp = ymax
  Anti-windup: I-action is off when u=umax
ysp = ymax
PI
This is simple CV-MV switching
u = input = manipulated variable (MV)
y = output = controlled variable (CV)
We satisfy the input saturation rule:
«When the MV (u) saturates, control of the CV (y) can be given up»

## Slide 32: Optimization with safety constraint
Example: Drive as fast as possible but safely
max y
s.t. y1 ≤ y1max
u ≤ umax
y2 ≥ y2min
(u=power, y=speed, y2=distance to car in front)
Disturbances (d): Slope of road, other cars
Optimal solution has three active constraint regions:
  CV=y1 = y1max = 120 km/h  speed limit
  MV=u = umax  max power (steep hill)
  CV=y2 = y2min  minimum distance (busy road)
Solved with two PI-controllers and min-selector («adaptive cruise control»)
  C1: Cruise controller with y1sp = y1max
  C2: Distance controller with y2sp= y2min
  Both controllers need anti-windup (turn off when inactive)
MIN
u1
u2
u=min(u1,u2)
c1
c2
y1
y2
PI
All three constraints are satisfied with a small u
Selector: This is CV-CV switching

## Slide 33: Anti-windup
All the controllers shown need anti-windup to «stop integration» during periods when the control action (vi) is not affecting the process:
  Controller is disconnected (because of selector)
  Physical MV ui is saturated
Anti-windup using back-calculation. Typical choice for tracking constant, KT=1
KT,i
Selector or
saturation

## Slide 34: Design of selector structure
Rule 1 (max or min selector)
Use max-selector for constraints that are satisfied with a large input
Use min-selector for constraints that are satisfied with a small input
Rule 2 (order of max and min selectors):
If need both max and min selector: Potential infeasibility
Order does not matter if problem is feasible
If infeasible: Put highest priority constraint at the end
“Systematic design of active constraint switching using selectors.” Dinesh Krishnamoorthy , Sigurd Skogestad. Computers & Chemical Engineering, 2020

## Slide 35: Valves have “built-in” selectors
A min-flow (z=0) gives a “built-in” max-selector (to avoid negative flow)
A max-flow (z=1) gives a “built-in” min-selector
So it’s not necessary to add these as selector blocks (but it will not be wrong).
  Both will always be satisfied because physical input constraints can never be violated.
  There is no danger of infeasibility /inconsistency here because we cannot have both z=0 and z=1 at the same time.

## Slide 36: Anti-surge control
Minimize compression cost but keep safe operation (F>Fmin)
min u
s.t. y ≥ ymin (safety constraint)
u ≥ umin = 0
(u= FR=recycle flow, y=F=flow in compressor)
Disturbance (d): Feed flow F0
Optimal solution has two active constraint regions:
  CV=y = ymin (for small F0)
  MV=u = umin = 0 (for large F0)
Solved with PI-controller («anti-surge control»)
  ysp = ymin
  Anti-windup: I-action is off when u=umin=0
F0
y=F
u=FR
FC
Fsp=Fmin
MAX
umin=0
MAX-block to avoid negative flow.
Not needed because the input (valve) has «built-in» u ≥ 0.
ysp = ymin
PI
This is simple CV-MV switching
We satisfy the input saturation rule:
«When the MV (u) saturates, control of the CV (y) can be given up»

## Slide 37: Furnace control
TC
u=Fuel gas
Flue gas
Process fluid (water)
Air
T1s = 500C
TC
T2max=700C
y1=T1
uA
uB
u=min(uA,uB)
Input (MV)
u = Fuel gas flowrate
Output (CV)
y1 = process temperature T1
(with desired setpoint)
y2 = furnace temperature T2
(max constraint)
Rule: Use min-selector for constraints that are satisfied with a small input
Selector: This is CV-CV switching
u = input = manipulated variable (MV)
y = output = controlled variable (CV)
MIN
“Systematic design of active constraint switching using selectors.” Dinesh Krishnamoorthy , Sigurd Skogestad. Computers & Chemical Engineering, 2020
with safety constraint
y2=T2
HP steam

## Slide 38: Example: Furnace control
TC
u=Fuel gas
Flue gas
Process fluid
Air
T1s = 500C
TC
T2max=700C
LS
y1=T1
y2=T2
uA
uB
u=min(uA,uB)
Furnace control : Cannot give up control of y1=T1. What to do?
Inputs (MV)
u = Fuel gas flowrate
u2 = Process flowrate
Output (CV)
y1 = process temperature T1
(with desired setpoint)
u2
MIN

## Slide 39: Cannot give up controlling T1 Solution: Cut back on process feed (u2) when T1 drops too low
TC
u=Fuel gas
Flue gas
Process fluid
Air
T1s = 500C
TC
T2max=700C
LS
y1=T1
y2=T2
uA
uB
u=min(uA,uB)
TC
T’1s = T1s-5C=495C
u2
TC
Using Input-input switching
Inputs (MV)
u = Fuel gas flowrate
u2 = Process flowrate
Output (CV)
y1 = process temperature
(with desired setpoint)
Note: Standard Split Range Control is not good here.
Could be two reasons for too little fuel
  Fuel is cut back by override (safety)
  Fuel at max,
So don’t know limit for MV1 to use in SRC-block.
This is complex CV-MV switching
u = input = manipulated variable (MV)
y = output = controlled variable (CV)
MIN

## Slide 40: Cannot give up controlling T1 Solution: Cut back on process feed (u2) when T1 drops too low
TC
u=Fuel gas
Flue gas
Process fluid
Air
T1s = 500C
TC
T2max=700C
LS
y1=T1
y2=T2
uA
uB
u=min(uA,uB)
Inputs (MV)
u = Fuel gas flowrate
u2 = Process flowrate
Output (CV)
y1 = process temperature
(with desired setpoint)
TC
T’1s = T1s-5C=495C
u2
This is complex CV-MV switching
u = input = manipulated variable (MV)
y = output = controlled variable (CV)
MIN
  Solution: Two controllers with different setpoints

## Slide 41: Summary constraint switching: Only three different cases (or maybe four)
MV-MV switching
  Need many MVs to cover whole steady-state range
  Use only one MV at a time
  Three options: 1. Split range control, 2. Different setpoints, 3. Valve position control (VPC)
CV-CV switching («override»)
  Must select between CVs
  Only one option: Many controllers with Max-or min-selector
CV-MV switching (because MV saturates)
3A. Simple: CV can be given up (follow «input saturation rule»)
  Don’t need to do anything (except anti-windup in controller)
3B. Complex: CV cannot be given up
  Combine MV-MC switching (three options) with CV-CV switching (selector)
Process
Process
Process
Process

## Slide 42: Oops…out of time
Because the timr for the plenary was reduced from 60 to 40 minutes because of delays, I only got to this point during my presentation in Toulouse
But I think it was enough to give the audience the message:
  Put optimization into the control layer whenever feasible
  It’s a complement and not alternative to online model-based optimization

## Slide 43: 5. Systematic procedure for designing control system that achieves optimal operation

## Slide 44
Use of models and data
u = valves
RTO layer:
Nonlinear model of whole process
usually physical and static
MPC layer:
Multivariable dynamic linear model for each unit
usually from data
PID-layer:
Dynamic linear model for each loop
usually from data.
PROCESS
H2
H
y1=CV1
y2=CV2
y1s
y2s
y = all measurements (online data)
d
ny
Data reconciliation (static)
Or
Estimator (e.g. EKF)
Nonlinear model
MPC
d, x
^ ^

## Slide 45: Systematic procedure for designing plantwide control system
Start “top-down” with economics:
Step 1: Define operational objectives and constraints
Step 2: Optimize steady-state operation
Step 3: Decide what to control (CV1 and CV2)
Step 4: Choose TPM location
Then design control system bottom-up:
Step 5: Regulatory control
Step 6: “Advanced/supervisory control” system
Step 7: Real-time optimization (Do we need it?)
S. Skogestad, ``Control structure design for complete chemical plants‘’, Computers and Chemical Engineering, 28 (1-2), 219-234 (2004).
Process
MVs

## Slide 46: Example: Bicycle riding Note: Design starts from the bottom
Regulatory control (step 5):
  First need to learn to stabilize the bicycle
    CV2 = y2 = tilt of bike
    MV = body position
Supervisory control (step 6):
  Then need to follow the road.
    CV1 = y1 = distance from right hand side
    MV=CV2s
  Usually a constant setpoint policy is OK, e.g. y1s=0.5 m
Optimization layer (step 7):
  Which road to follow?
  RTO = GPS
Hierarchical decomposition

## Slide 47: Systematic design of simple advanced controllers (APC)
First design simple control system for nominal operation
  With single-loop PID control we need to make pairing between inputs (MVs) and outputs (CVs):
  Should try to follow two rules
    «Pair close rule» (for dynamics). Pair such that we have small effective delay and large gain
      This is to get fast control and avoid instability
    «Input saturation rule»: «Pair MV that may saturate with CV that can be given up (at least when the MV constraint is reached)”.
      This avoids loss of control
      Gives simple CV-MV switching
Process

## Slide 48: Systematic design of simple advanced controllers (APC)
First design simple control system for nominal operation
  With single-loop PID control we need to make pairing between inputs and outputs:
  Should try to follow two rules
    «Pair close rule». Pair such that we have fast reponse and large gain
      This is to get fast control and avoid instability
    «Input saturation rule»: «Pair MV that may saturate with CV that can be given up”.
      This avoids loss of control
      Gives simple CV-MV switching
Then make a list of possible new contraints that may be encountered (because of disturbances, parameter changes, price changes)
Reach constraint on new CV
  Simplest: Find an unused input (simple CV-MV switching)
  Otherwise: CV-CV switching using selector
Reach constraint on MV (which is used to control CV)
  Simplest (If we followed input saturation rule):
    Can give ip controlling CV (Simple CV-MV switching)
    Don’t ned to do anything
  Otherwise (if we cannot give up controlling CV)
    Simplest: Find an unused input
      MV-MV switching
    Otherwise: Pair with a MV that already controls another CV
      Complex CV-MV switching
      Must combine MV-MV and CV-CV switching
Is this always possible? No, pairing inputs and outputs may be impossible with many constraints.
May then use MPC instead

## Slide 49
Disturbance
F2 [m3/s]
Example : Level control
LC
SP
FC
F1,m
F1,s
F1 [m3/s]
u1 = z1 (inflow valve position)
u2 = z2 (outflow valve position) (likely to saturate)
y1 = F1 (inflow): Should be controlled at setpoint F1,s (if possible)
y2 = level: must always be controlled (at some SP)
Problem: outflow-valve may saturate at fully open (z2=1) and then we lose level control
Note: We did not following the “input saturation rule” which says:
Pair MV that may saturate (z2) with CV that can be given up (F1)
z2
z1
Nomimal design with “pair-close” rule
Process

## Slide 50
Disturbance
LC
Nominal design with Reverse pairing (follows “input saturation rule”):
FC
SP
F1,m
F2,s
BUT with Reverse pairing: Get “long loop” for flow control
In addition: loose control of y2= level if z1 (F1-valve) saturates
F1 [m3/s]
F2 [m3/s]
«long loop»
This gives simple CV-MV switching (if z2 saturates at fully open)
«Long loop» = Works through other loops

## Slide 51
Disturbance
LC
FC
SP-L
F1,m
F1,s
Alternative solution: Follow “Pair close”-rule and use Complex CV-MV switching.
When z2 saturates at max, use the other MV (z1) for level control and give up controlling F1
Get: “Bidirectional inventory control”
LC
SP-H
MIN
F1 [m3/s]
F2 [m3/s]
Avoid long loop for control of F1
Works both when F1-valve or F2-valve saturate at open
Overall: seems to be the best solution
LC
Using
MV-MV
switching
This is complex CV-MV switching

## Slide 52
Disturbance
LC
FC
SP-L
F1,m
F1,s
Recommended: Two controllers
SP-L = low level setpoint
SP-H = high level setpoint
LC
SP-H
MIN
F1 [m3/s]
F2 [m3/s]
Use of two setpoints is good for using buffer dynamically!!
Alternative solution: Follow “Pair close”-rule and use Complex CV-MV switching.
When z2 saturates at max, use the other MV (z1) for level control and give up controlling F1
Get: “Bidirectional inventory control”
This is complex CV-MV switching

## Slide 53: Generalization of bidirectional inventory control

## Slide 54
TPM = throughput manipulator
(located at bottleneck = flow constraint)
Radiation rule for
Inventory control
(Georgakis)
«Inventory loops are radiating around given flow (TPM)»
Follows «pair-close» rule
Avoids «long loops» for inventory control

## Slide 55
Very smart selector strategy: Bidirectional inventory control
Reconfigures automatically with optimal buffer management!!
F.G. Shinskey, «Controlling multivariable processes», ISA, 1981
Max flow:
Fs=∞
Cristina Zotica, Krister Forsman, Sigurd Skogestad ,»Bidirectional inventory control with optimal use of
intermediate storage», Computers and chemical engineering, 2022
,

## Slide 56: New example: Optimal operation of a cooler

## Slide 57: Example: Optimal control of a cooler
Main control objective:
y1=TH=THsp
Secondary objective (can be given up)
y2= FH=FHsp
Manipulated Variables:
u1=zC , u2=zH
Both valves may satúrate at max
Disturbance:
TCin
Cooling water

## Slide 58: Optimization of Cooler
max y2 (throughput)
s.t. y1 = y1sp  temperature
u1 ≤ u1max
u2 ≤ u2max  max. throughput
y2 ≤ y2sp  desired throughput
Active constraint regions:
  y1 = y1sp, y2 = y2sp  Nomimal = unconstrained
  y1 = y1sp, u2 = u2max
  y1 = y1sp, u1 = u1max
Input saturation pairing rule: It’s not possible to follow this rule since both MVs may saturate…
Will pair y1 with u1 for dynamic reasons («pair close rule»)
And use «complex» CV-MV switching logic when u1 saturates

## Slide 59: Pairings at nominal «unconstrained» operating point
FC may saturate for a
large disturbance (TCin)
Use FC to control TH

## Slide 60: Alt.1: Split range control with min-selector
Tuning of TC using SIMC rule:
  τc = 2θ = 88 s
  Kc = -0.55
  τI = 74 s
Complex CV-MV switching
=26C

## Slide 61: Alt.2 . Two controllers/setpoints and min-selector
Complex CV-MV switching
=26C
=27C

## Slide 62: Alt. 3 VPC with min-selector
Complex CV-MV switching

## Slide 63
Alt. 1 Split range control
Alt. 3 Valve position control
Alt. 2 Two controllers/setpoints
Disturbances: Tcin +2◦C at t = 200 s, Tcin additional +4 ◦C at t = 2000 s.
Complex CV-MV switching

## Slide 64: MPC for cooler
For represents the flow at the nominal point.
 Objective function
(CV constraints)
Model 
MV constraints 
Tuning  trial and error

## Slide 65: MPC vs Split range Control (PI)
Disturbance (TCin)
t = 10 s; + 2°C
t = 1000 s; + 4°C
Yellow: MPC:
Δt = 50 s
ω₁ = 3
ω₂ = 0.1
FC
FH
TH
Red: Split Range Control (PI)

## Slide 66: Many people think they need to use MPC if they encounter constraints
True only for more complicated multivariable cases
In most cases PI(D)-control is simpler and equallly good
  Need anti-windup on the controller
=26C

## Slide 67: Model predictive control (MPC)
Can include constraints explicitly
If lack of DOF to meet control specifications:
  Conventional: Use weights
    (Partially) give up variables with small weights in objective function.
  Use two-stage MPC with constraint priority list:
    Stage 1. Check for steady-state feasibility and give up low-priority constraints if necessary
    Stage 2. Solve conventional dynamic MPC

## Slide 68: 6. Conclusion
Put optimization into the control layer
  It’s much faster and more effective
Conventional APC works very well in many cases
  Optimization by feedback
    Self-optimizing control
    Active constraint switching
  Need to pair input and output.
    Advantage: The engineer can specify directly the solution
    Problem: May not be possible for complex cases
  Need model only for parts of the process (for tuning)
  Challenge: Need better teaching and design methods