## Slide 1: Overview and Classification of online process optimization approaches
IFAC DYCOPS Pre-symposium workshop
Sigurd Skogestad
Johannes Jäschke
Dinesh Krishnamoorthy

## Slide 2
Trondheim

## Slide 3: Presenters
Sigurd Skogestad
Professor NTNU
PhD Caltech (1987)
Johannes Jäschke
Associate Prof. NTNU
PhD NTNU (2011)
Dinesh Krishnamoorthy
PhD student NTNU (2019)
MS Imperial College (2012)

## Slide 5: Agenda
13:30 – 13:50 | Welcome and info
13:50 – 14:00 | Introduction Real time optimization (Sigurd Skogestad)
14:00 – 14:10 | 1. Conventional approach: Steady-state optimization - and challenges (Sigurd Skogestad)
14:10 – 14:40 | 2. Academic approach: Economic MPC and Dynamic RTO (Johannes Jäschke)
14:40 – 15:00 | 3. Steady-state optimization with transient measurements – Hybrid RTO (Dinesh Krishnamoorthy)
15:00 – 15:20 | 4. Feedback-based RTO using model-based gradient estimation (Dinesh Krishnamoorthy)
15:20 – 15:40 | 5. Extremum seeking control (Dinesh Krishnamoorthy)
15:40 – 16:00 | Coffee Break
16:00 – 16:20 | 6. Modifier Adaptation (Johannes Jäschke)
16:20 – 16:40 | 7. Self-optimizing Control (Sigurd Skogestad)
16:40 – 17:00 | 8. Classical Approach: Optimal operation using conventional advanced control (Sigurd Skogestad
17:00 – 17:30 | The different approaches are complementary, not contradictory! (Johannes Jäschke)
17:30 – 18:00 | Discussion and Concluding remarks (all)

## Slide 7: Introduction to Real time optimization
IFAC DYCOPS Pre-symposium workshop
Sigurd Skogestad

## Slide 8: Main objectives control system
ARE THESE OBJECTIVES CONFLICTING?
Usually NOT
  Different time scales
    Stabilization fast time scale
  Stabilization doesn’t “use up” any degrees of freedom
    Reference value (setpoint) available for layer above
    But it “uses up” part of the time window (frequency range)
Economics: Implementation of acceptable (near-optimal) operation
Regulation: Stable operation

## Slide 9
In theory: Centralized controller is always optimal (e.g., EMPC)
Objectives
Present state
Model of system
Approach:
  Model of overall system
  Estimate present state
  Optimize all degrees of freedom
Process control:
  Excellent candidate for centralized control
Problems:
  Model not available
  Objectives = ?
  Optimization complex
  Not robust (difficult to handle uncertainty)
  Slow response time
(Physical) Degrees of freedom, u= valve positions
CENTRALIZED
OPTIMIZER

## Slide 10: In practice: Hierarchical decision system based on time scale separation
Manager
Process engineer
Operator/RTO
”Advanced classical control”/MPC
PID-control
u = valves
min J (economics)
Setpoint control
(+ look after other variables)
Stabilize + avoid drift
Focus of this workshop

## Slide 11: General objective process operation (RTO): Minimize cost J = maximize profit (–J) [$/s] subject to constraints
Typical process constraints:
  Product quality (purity)
  Environment (amount and purity of waste products)
  Equipment (max. and min. flows, pressures)
Typical degrees of freedom (decision variables) (u)
  Flowrates: Feeds, splits (recycles), heating/cooling
where
= price of feed [$/kg] x feed flow rate [kg/s]
= price of utility (energy) x energy usage
= price (value) of product x product flow rate
Note: No capital costs or costs for operators
(assumed fixed for time scale of interest, a few hours)

## Slide 12: Two main operation modes
  I. Sales limited by market: Given production (constraint)
    Optimal with high energy efficiency (good for environment)
  II. High price product and high demand: Maximize production
    Lower energy efficiency
    Optimal to overpurify waste products to recover more (good for environment)

## Slide 13: Formulation of Real time optimization
Process Model
Process constraints
Optimal decision variables (u) / Optimal setpoints (y)
Economic Model
s.t.
Internal variables
Decision variables
d: Parameter values / disturbances

## Slide 14: 1. Conventional approach: Steady-state Real time optimization - and Challenges
IFAC DYCOPS Pre-symposium workshop
Sigurd Skogestad

## Slide 15: Conventional (commercial) steady-state RTO
D. E. Seborg, D. A. Mellichamp, T. F. Edgar, F. J. Doyle III, Process dynamics and control, John Wiley & Sons, 2010.
Steady-state models
Two-step approach
  “Data reconciliation”:
    Steady-state detection
    Update estimate of d: model parameters, disturbances (feed), constraints
  Re-optimize to find new optimal steady state
Data reconciliation
dhat
d

## Slide 16: Conventional steady-state RTO
Typically uses detailed process models with full thermo package
  Hysys / Unisim (Honeywell)
  Aspen
  PROCESS
  …..
But traditional RTO less used in practice than one should expect
  Ethylene plants (furnace)
  Some refinery applications

## Slide 17: Why is conventinal static RTO not commonly used?
Cost of developing and updating the model (costly offline model update)
Wrong value of model parameters and disturbances d (slow online model update)
Not robust, including computational issues
Frequent grade changes make steady-state optimization less relevant
Dynamic limitations, including infeasibility due to (dynamic) constraint violation
Incorrect model structure
Problems (in expected order of importance):
Not problems, but Challenges 

## Slide 18: Challenge 1 - Costly offline model development and update
Lack of domain/expert knowledge
Change in process configuration
Model simplification
Possible Fix: Data-methods based on measuring Cost (J) (Extremum seeking control; see Approach 5)
Recent interest – Machine learning and AI to develop models

## Slide 19: Challenge 2 - Steady-state wait time
  Frequent disturbances (d)
  Long settling times
Data reconciliation step is infrequent
Wrong value of model parameter/disturbances (dhat)
Process operates sub-optimally for long periods of time
Data reconciliation
dhat
Fix: Use dynamic model in estimation step (Hybrid RTO; see Approach 3)
d

## Slide 20: Challenge 3 - Computational issues
Convergence issues and numerical failure
CPU times
scaling of variables
Complementary constraints
Fix – Methods that do not need to solve numerical optimization problems online (Novel Feedback RTO; see Approach 4)

## Slide 21: Challenge 4 - Frequent grade changes
  Continuous process with frequent changes in feed, product specifications, market disturbances, slow dynamics/long settling time
  Continuous with frequent grade transitions
  Batch processes
  Cyclic operations
Fix (if relevant) – Dynamic optimization methods (DRTO or EMPC; see Approach 2)
Source: Koller et al. (2017) Comput& Chem Eng, 106, pp.147-159.

## Slide 22: Challenge 5 - Dynamic limitations
Dynamic constraint violations
Force variables to fixed set points, may not utilize all degrees of freedom
A steady-state optimization layer and a control layer may lead to model inconsistency
Partial Fix – Use setpoint tracking control layer below RTO

## Slide 23: Challenge 6 – Incorrect model structure
E.g. missing one chemical reaction
Cannot be fixed by parameter updates
Fix – Modifier adaptation based on measuring Cost (J)

## Slide 24: 2. Academic approach : Dynamic RTO and Economic MPC
IFAC DYCOPS Pre-symposium workshop
Johannes Jäschke

## Slide 25: DRTO and Economic MPC
  Optimize not only steady state, but also transients
  Continuous process with frequent changes in feed, product specifications, market disturbances, slow dynamics/long settling time
  Continuous with frequent grade transitions
  Batch processes
  Energy storage
  Cyclic operations
Directly address challenge 4 (frequent changes, non-negligible transient operation)
Source: Koller et al. (2017) Comput& Chem Eng, 106, pp.147-159.

## Slide 26: Dynamic RTO
Uses dynamic models online
Repeatedly solve Dynamic RTO problem for a given horizon
Closely related to economic MPC

## Slide 27: Main idea
future
past
states
manipulated variable sent to lower layer
prediction horizon
estimation horizon
measurements
Repeatedly solve

## Slide 28: Main idea
Repeatedly solve

## Slide 29: Economic MPC ~ Dynamic RTO
Centralized “All-in-one” optimizer
Higher sampling rates
Hierarchical layers with time scale separation
Lower sampling rates
Usually in Economic MPC a lower layer is also included, e.g. perfect level control, etc..

## Slide 30: Industrial applications of Dynamic RTO
Bartusiak (2007)
  polyolefin polymerization processes
Odloak+Petrobras
  FCC unit
Cybernetica
  Polymerization reactors
HVAC (Stanford) Rawlings

## Slide 31: Challenges with Dynamic RTO
Main Challenge: Manage complexity
Trade-off
Cost to make it work and improved profit.

## Slide 32: Complexity: The challenge with Dynamic RTO
Obtaining and maintaining an accurate dynamic model
Computational issues
Robustness issues
Implementation issues

## Slide 33: Obtaining and maintaining an accurate dynamic model
  Modelling efforts
  Requires plant testing over larger operation range
  Trade-off between learning model parameters and optimal operation

## Slide 34: Computational issues
  Computational cost for solving the large NLP
    NLP solvers (IPOPT (Biegler) Conopt, others…
    Fast Sensitivity-based methods
      Realtime iterations (Diehl et al 2002)
      Advanced step NMPC (Zavala & Biegler 2009, Jäschke et al 2015)
    Convergence issues
      Thermodynamics model crashes, Flash computations
  Discrete and nonsmooth decisions
    Lead to mixed integer optimization problems
    Cannot be solved in real-time for large systems

## Slide 35: Robustness issues
Robustness issues
  Model errors
  Uncertain parameters (predictions)
  Implications for stability
  Tend to make computations significantly more complex

## Slide 36: Implementation issues
Tuning, regularization weights in cost function
  Typical cost in practice (Bartusiak 2007)
Allowing for manual operations
What to put into which layer?
Measurement faults, reliable state and parameter estimation
Require many Ad-hoc problem-dependent solutions

## Slide 37: Academia
Stability
Numerical issues
  Computation speed
  Decentralizing
Uncertainty
  Stochastic MPC
  Robust MPC
  Chance constraint
  Dual MPC
Typically add complexity
Handle complexity in real-time
Proofs mainly of concern for academia

## Slide 38: DRTO and EMPC has many potential benefits
Reduced amount of off-spec product
Changing operational strategy:
  Agile operation switching productions
    Demand-side management
    Load-balancing services
For some processes, optimal operation is not at a steady state (Angeli 2011)
Promise: Truly optimal operation
  But that is hard/impossible to deliver

## Slide 39: 3. Steady-state optimization using Transient Measurements – Hybrid RTO
IFAC DYCOPS Pre-symposium workshop
Dinesh Krishnamoorthy
Krishnamoorthy, D., Foss, B. and Skogestad, S., 2018. Steady-state real-time optimization using transient measurements. Computers & Chemical Engineering, 115, pp.34-45.

## Slide 40: Why is traditional static RTO not commonly used?
Cost of developing and updating the model (costly offline model update)
Wrong value of model parameters and disturbances (slow online model update)
Not robust, including computational issues
Frequent grade changes make steady-state optimization less relevant
Dynamic limitations, including infeasibility due to (dynamic) constraint violation
Incorrect model structure

## Slide 41: Traditional Steady-state RTO

## Slide 42: Steady-state wait time
Transient measurements cannot be used
Large chunks of data discarded
Steady state detection issues
  Erraneously accept transient data
  Non-stationary drifts
Source: Kelly, J.D. and Hedengren, J.D., 2013. A steady-state detection (SSD) algorithm to detect non-stationary drifts in processes. Journal of Process Control, 23(3), pp.326-331.

## Slide 43: Steady-state wait time
Source: Câmara MM, Quelhas AD, Pinto JC. Performance Evaluation of Real Industrial RTO Systems. Processes. 2016, 4(4).
Based on statistical tests, e.g:
In practice - some heuristics

## Slide 44: How to address steady-state wait time?
OBVIOUS: DYNAMIC RTO
Dynamic RTO has problems – especially the optimization part

## Slide 45: Hybrid RTO
Dynamic Estimation
+
Static Optimization
Krishnamoorthy, D., Foss, B. and Skogestad, S., 2018. Steady-State Real-time Optimization using Transient Measurements. Computers and Chemical Engineering, Vol 115, p.34-45.

## Slide 46: Hybrid RTO
Krishanmoorthy, Foss, Skogestad, Comput & Chem Eng (2018) – Hybrid RTO
Matias & Le Roux, J. Proc. Control (2018) – ROPA
Valluru & Patwardhan, Ind. Eng. Chem. Res (2019) – Frequent RTO

## Slide 47: CASE STUDY: Gas lift
Main objective: Max oil prod.
Constraint: Max Gas capacity
Main disturbance (d): GOR variation
Reservoir
GOR = Gas/Oil ratio in feed (reservoir)
MV1
MV2
Notes: s.t.
max┬(𝑤_𝑔𝑙 )⁡ $_𝑜 ∑▒𝑤_𝑝𝑜 −$_𝑔𝑙 ∑▒𝑤_𝑔𝑙 −$_𝑓𝑙 𝑤_𝑓𝑙
s.t.
∑▒𝑤_𝑝𝑔 ≤𝑤_𝑔^𝑚𝑎𝑥+𝑤_𝑓𝑙

## Slide 48: Disturbance: GOR variation

## Slide 49: Typical measured data (pressures and flowrates)

## Slide 50: GOR estimation - using “data reconciliation” (traditional static RTO)
Problem: Steady-state wait time for data reconciliation

## Slide 51: GOR estimation – using extended Kalman filter (DRTO & HRTO)

## Slide 52: Oil and gas rates
SRTO = traditional static RTO
HRTO = hybrid RTO
DRTO = dynamic RTO

## Slide 53: Results
Chart: 
| SRTO | HRTO | DRTO
Integrated Profit | 1.8256 | 2.7019 | 2.7509
Chart: Computation Time [s]
| SRTO | HRTO | DRTO
avg. time | 0.0184 | 0.0199 | 0.9025
max time | 0.0223 | 0.0282 | 3.3631

## Slide 54: Advantage of steady-state optimization (SRTO & HRTO)
Computation time & numerical robustness
Avoids causality issue / index problems
Allows optimization on decision variables other than the MVs
  Simplifies the optimization
  Slower time scale (choose slow varying variables as decision variables)

## Slide 55: Why is traditional static RTO not commonly used?
Cost of developing and updating the model structure (costly offline model update)
Wrong value of model parameters and disturbances (slow online model update)
Not robust, including computational issues
Frequent grade changes make steady-state optimization less relevant
Dynamic limitations, including infeasibility due to (dynamic) constraint violation
Incorrect model structure

## Slide 56
MV2: Setpoint provided to tracking controller
Actual MV move by setpoint tracking controller
Dynamic limitations – not a big issue
SRTO = traditional static RTO
HRTO = hybrid RTO
DRTO = dynamic RTO

## Slide 57: Oil and gas rates
SRTO = traditional static RTO
HRTO = hybrid RTO
DRTO = dynamic RTO

## Slide 58: 4. Feedback RTO based on novel steady-state gradient estimation method
IFAC DYCOPS Pre-symposium workshop
Dinesh Krishnamoorthy
Krishnamoorthy, D., Jahanshahi, E. and Skogestad, S., 2019. Steady-state real-time optimization using transient measurements. Industrial and Engineering Chemistry Research 115, pp.34-45.

## Slide 59: Why is traditional static RTO not commonly used?
Cost of developing and updating the model structure (costly offline model update)
Wrong value of model parameters and disturbances (slow online model update)
Not robust, including computational issues
Frequent grade changes make steady-state optimization less relevant
Dynamic limitations, including infeasibility due to (dynamic) constraint violation
Incorrect model structure

## Slide 60: Necessary condition of optimality
The ideal controlled variable is the gradient
May use simple feedback controller to control the gradient to constant setpoint of zero.
Problem: We do not usually have gradients as measurements

## Slide 61
Feedback RTO
Krishnamoorthy, D., Jahanshahi, E. and Skogestad, S., 2018. A feedback real-time optimization strategy, Ind. Eng. Res. Chem

## Slide 62
Hybrid RTO
Feedback RTO
Feedback RTO: Replace steady-state optimization by feedback control
Krishnamoorthy, D., Jahanshahi, E. and Skogestad, S., 2018. A feedback real-time optimization strategy, Ind. Eng. Res. Chem (submitted).

## Slide 63
Feedback RTO
Krishnamoorthy, D., Jahanshahi, E. and Skogestad, S., 2018. A feedback real-time optimization strategy, Ind. Eng. Res. Chem (submitted).

## Slide 64: Feedback RTO
Krishnamoorthy, D., Jahanshahi, E. and Skogestad, S., 2018. A feedback real-time optimization strategy, Ind. Eng. Res. Chem (submitted).

## Slide 65
CSTR case study
Economou, C. G.; Morari, M.; Palsson, B. O. Internal model control: Extension to nonlinear system. Industrial & Engineering Chemistry Process Design and Development 1986, 25, 403–411.
Ye, L.; Cao, Y.; Li, Y.; Song, Z. Approximating Necessary Conditions of Optimality as Controlled Variables. Industrial & Engineering Chemistry Research 2013, 52, 798–808.

## Slide 66
Comparison of RTO approaches: MV
t = 400 s, d1: Increase CAin
t = 1400 s, d2: Increase CBin
closer look
SRTO = traditional static RTO
HRTO = hybrid RTO
DRTO = dynamic RTO
New method = Feedback RTO

## Slide 67
Comparison of RTO approaches
Chart: Computation time
| Feedback RTO | SRTO | HRTO | DRTO
 | 0.004 | 0.007 | 0.01 | 0.14
Chart: Integrated Loss
| Feedback RTO | SRTO | HRTO | DRTO
 | 248.07 | 342.38 | 257.97 | 247.68
2
4
3
1
248.1
342.3
257.1
247.1

## Slide 68
Feedback RTO - Other case studies
Evaporator process1
Gas lift wells2
Ammonia reactor3
Krishnamoorthy, D., Jahanshahi, E. and Skogestad, S., Control of steady-state gradient for an Evaporator process, PSE Asia (Submitted 2019)
Krishnamoorthy, D., Jahanshahi, E. and Skogestad, S., 2018. Gas-lift Optimization by Controlling Marginal Gas-Oil Ratio using Transient Measurements (in-Press), IFAC OOGP, Esbjerg, Denmark
Bonnowitz, H., Straus, J., Krishnamoorthy, D., and Skogestad, S., 2018. Control of the Steady-State Gradient of an Ammonia Reactor usingTransient Measurements, Computer aided chemical engineering, Vol.43, p.1111-1116 (ESCAPE 28)

## Slide 69: CASE STUDY: Gas lift
Main objective: Max oil
Constraint: Max Gas
Main disturbance (d): GOR variation
Reservoir
GOR = Gas/Oil ratio in feed (reservoir)
MV1
MV2
Notes: s.t.
max┬(𝑤_𝑔𝑙 )⁡ $_𝑜 ∑▒𝑤_𝑝𝑜 −$_𝑔𝑙 ∑▒𝑤_𝑔𝑙 −$_𝑓𝑙 𝑤_𝑓𝑙
s.t.
∑▒𝑤_𝑝𝑔 ≤𝑤_𝑔^𝑚𝑎𝑥+𝑤_𝑓𝑙

## Slide 70
Marginal Gas-Oil Ratio (mGOR)
Marginal GOR

## Slide 71
Unconstrained case

## Slide 72
Control Structure

## Slide 73
Simulation Results

## Slide 74: Multivariable Example: Ammonia Reactor

## Slide 75: Results

## Slide 76: Results

## Slide 77: 5. Extremum Seeking Control
IFAC DYCOPS Pre-symposium workshop
Dinesh Krishnamoorthy

## Slide 78: Why is traditional static RTO not commonly used?
Cost of developing and updating the model (costly offline model update)
Wrong value of model parameters and disturbances (slow online model update)
Not robust, including computational issues
Frequent grade changes make steady-state optimization less relevant
Dynamic limitations, including infeasibility due to (dynamic) constraint violation
Incorrect model structure

## Slide 79: Necessary condition of optimality
The ideal controlled variable is the gradient
May use simple feedback controller to control the gradient to constant setpoint of zero.
Problem: We do not usually have gradients as measurements

## Slide 80: Data-driven method
We do not use a model to estimate the gradient
Estimate gradient Experimentally
  NB! Need Cost measurement
Similar approaches
  Extremum seeking
  NCO tracking
  Hill climbing control
  Experimental optimization
  ....
Difference is in the way gradient is estimated

## Slide 81: Steady-state gradient
J
u
Francois & Bonvin (2007)
Jäschke & Skogestad(2011)

## Slide 82: Classical Extremum seeking control
Gradient Estimation
Integral action
Draper & Li (1951)
Krstic & Wang (2000)

## Slide 83: Sinusoidal perturbation
J
u
Special case of Fast Fourier Transform (FFT) - single frequency case

## Slide 84: Extremum Seeking Control
Probe the system
Observe how the cost changes
Estimate Gradient
Decide which way to move

## Slide 85: Classical Extremum Seeking Control
Needs time scale separation to approximate plant as static map
Prohibitively slow convergence for systems with slow dynamics
Typically 100 times slower than the system dynamics !
Can we remove the static map assumption?
Come to my talk at....

## Slide 86: CASE STUDY: Gas lift well
Reservoir
GOR = Gas/Oil ratio in feed
MV1
Notes: s.t.
max┬(𝑤_𝑔𝑙 )⁡ $_𝑜 ∑▒𝑤_𝑝𝑜 −$_𝑔𝑙 ∑▒𝑤_𝑔𝑙 −$_𝑓𝑙 𝑤_𝑓𝑙
s.t.
∑▒𝑤_𝑝𝑔 ≤𝑤_𝑔^𝑚𝑎𝑥+𝑤_𝑓𝑙

## Slide 87: Least square Extremum seeking control
Fit a linear model
Using least squares fit
Hunnekens et al. (2011)

## Slide 88: Least square Extremum seeking control
u
Image source: Hunnekens et al. (2011)

## Slide 89: Other gradient estimation schemes
Multiple units (Srinivasan et al. 2007)
Recursive least squares estimation (Chioua, 2016)
Phasor based extremum seeking control (Trolleberg & Jacobsen, 2012)
... and some other model-based schemes
Neibhouring extremals (Gros et al. 2009)
Parameter estimation (Adetola & Guay, 2007)

## Slide 90: Issues with Extremum seeking
Need Cost measurement
  Often cost function is a sum of several terms
  All terms must be measured
  Estimation of cost requires model (dependency on model – no longer model free)
Time scale separation
  Process dynamics affects gradient estimation
  Prohibitively slow convergence to the optimum
Constant probing of the system
Unknown and abrupt disturbances affects gradient estimation
ESC more suited for single units, but not for entire chemical plants

## Slide 91: Effect of abrupt disturbances
d1
d2

## Slide 92: Measured disturbance handled using feedforward

## Slide 93: 6. Modifier Adaptation
IFAC DYCOPS Pre-symposium workshop
Johannes Jäschke

## Slide 94: Why is traditional static RTO not commonly used?
Cost of developing and updating the model (costly offline model update)
Wrong value of model parameters and disturbances (slow online model update)
Not robust, including computational issues
Frequent grade changes make steady-state optimization less relevant
Dynamic limitations, including infeasibility due to (dynamic) constraint violation
Wrong model structure

## Slide 95: Modifier adaptation addresses the problem of plant model mismatch
RTO
Supervisory control (MPC)
Regulatory control
Process
from RTO (setpoints)
Cost
Input
Optimal input
From model
Optimal input
of the plant
Loss
Mismatch between model and plant leads to performance loss

## Slide 96: Modifier adaptation addresses the problem of plant model mismatch
RTO
Supervisory control (MPC)
Regulatory control
Process
from RTO (setpoints)
Cost
Input
Optimal input
From model
Optimal input
of the plant
Loss
Mismatch between model and plant leads to constraint violations (infeasibility)
Infeasible for plant

## Slide 97: Possible solutions
Find a better model
  Better parameters
  Better structure (that matches the plant better)
Modify optimization problem directly (Marchetti et al, 2009, Gao et al 2016)
  Use plant measurements
  No need to have an exact model
Marchetti et al. 2009, Ind. Eng. Chem. Res., 48 (13), pp 6022–6033
Gao et al.2016 Comp. & Chem. Eng. 91, pp 318–328

## Slide 98: How should modify the optimization problem
Key idea
  Add modifiers to make “optimality conditions” of the plant and optimality conditions of the model match
Iteratively repeat the optimization at sample times .
Plant Optimization problem
s.t.
Model optimization problem
s.t.

## Slide 99: How should modify the optimization problem
Key idea
  Add modifiers to make “optimality conditions” of the plant and optimality conditions of the model match
Iteratively repeat the optimization at sample times .
Plant Optimization problem
s.t.
Modified model optimization problem
s.t.

## Slide 100: Modifiers to match plant derivatives
Plant and modified model function gradients are equal
And
Input
Constraints
Cost and constraint gradients are modified to match Plant and model optimum coincide

## Slide 101: How to compute modifiers
Zero order modifiers
First order modifiers
Gradients from real plant

## Slide 102: Challenges
Finding gradients of the plant
Requires excitation
  Finite differences (Marchetti et al. 2009),
    Experiments and past points
  Broydens method
  Gradients from fitted surface (Gao et al 2016, Matias, J. 2019)
  Dynamic model identification (using transient data)
  Parallel units (Srinivasan 2007)

## Slide 103: Case Study
Gas lifted oil well
2Degrees of freedom
Constraints:
  Max gas lift for each well
  Max total gas handling capacity
Objective

## Slide 104: Case Study – Plant-model mismatch
Blue dashed line: max gas constraint
Black dashed line: max individual gas flow rate
Plant
Model

## Slide 105: Iterative RTO using Modifier adaptation
Circle: and Diamond:
Points from: MA-RTO iterations
Stars: Probing point for estimating gradients

## Slide 106: Alternative: Output modifier adaptation
Instead of adjusting cost and constraints, adjust output model
Modified RTO problem
s.t.
Cost and constraint gradients are modified to match Plant and model optimum coincide
Marchetti et al 2009

## Slide 107: Conclusion
A effective way to handle plant-model mismatch
  Combines properties from model-based and data-based optimization
Optimization problem is updated using plant gradient estimates
  Same gradient estimation problems as ESC
Iteratively converges to an optimum.
  Relatively slow, but we start at a better point (from the model).
  Can (should) be combined with other approaches
  Better than doing nothing, and living with the mismatch
Other refinements
  Decentralized schemes (Schneider et al. 2018)
  Second order modifiers (Faulwasser, Bonvin 2014)

## Slide 108: 7. Self-optimizing control “Move the optimization into the control layer”
IFAC DYCOPS Pre-symposium workshop
Sigurd Skogestad

## Slide 109: Do we really need real-time optimization?
Often not!
We often know or can guess the active constraints
  Example: Assume it’s optimal with max. reactor temperature
  No need to have a comples dynamic model with energy balance to find the optimal cooling
  Just use a PI-controller
    CV = reactor temperature
    MV = cooling

## Slide 110: Systematic procedure for economic process control
Start “top-down” with economics (steady state):
Step 1: Define operational objectives (J) and constraints
Step 2: Optimize steady-state operation
Step 3: Decide what to control (CVs)
  Step 3A: Identify active constraints = primary CV1.
  Step 3B: Remaining unconstrained DOFs: Self-optimizing CV1 (find H)
Step 4: Where do we set the throughput? TPM location
Then bottom-up (dynamics):
Step 5: Regulatory control
  Control variables to stop “drift” (sensitive temperatures, pressures, ....)
Finally: Make link between “top-down” and “bottom up”
Step 6: “Advanced/supervisory control”
    Control economic CVs: Active constraints and self-optimizing variables
    Look after variables in regulatory layer below (e.g., avoid saturation)
Step 7: Real-time optimization (Do we need it?)
S. Skogestad, ``Control structure design for complete chemical plants'',
Computers and Chemical Engineering, 28 (1-2), 219-234 (2004).
CV1
CV2
Process
MVs
RTO

## Slide 111
Optimizer (RTO)
PROCESS
Supervisory controller (MPC)
Regulatory controller (PID)
H2
H
y
ny
d
Stabilized process
Physical
inputs (valves)
Optimally constant valves
Always active constraints
CV1s
CV1
CV2s
CV2
Engineer: Must choose what to control in both layers (H2 and H)

## Slide 112: Step 1. Define optimal operation (economics) Usually steady state
Minimize cost J = J(u,x,d)
  subject to:
  Model equations: f(u,x,d) = 0
  Operational constraints: g(u,x,d) < 0
  u = degrees of freedom
  x = states (internal variables)
  d = disturbances
J = cost feed + cost energy – value of products
J
uopt
Jopt
Typical cost function in process control:

## Slide 113: (a) Identify degrees of freedom (b) Optimize for expected disturbances
Need good model, usually steady-state is OK
Optimization is time consuming! But it is offline
Main goal: Identify ACTIVE CONSTRAINTS
A good engineer can often guess the active constraints
Step 2. Optimize
J
uopt
Jopt
constraint

## Slide 114: Active constraints
Active constraints:
  variables that should optimally be kept at their limiting value.
Active constraint region:
  region in the disturbance space defined by which constraints are active within it.
Region 1
Region 2
Region 3
Disturbance 1
Disturbance 2
Optimal operation:
Need to switch between regions using control system

## Slide 115: How many active constraints regions?
Maximum:
  nc = number of constraints
BUT there are usually fewer in practice
Certain constraints are always active (reduces effective nc)
Only nu can be active at a given time
  nu = number of MVs (degrees of freedom)
Certain constraints combinations are not possibe
  For example, max and min on the same variable (e.g. flow)
Certain regions are not reached by the assumed disturbance set
Distillation
nc = 5
  25 = 32
xB always active
2^4 = 16
-1 = 15
In practice = 8

## Slide 116
Have found the optimal way of operation. How should it be implemented?
What to control ? (CV1).
  Active constraints
  Self-optimizing variables (for unconstrained degrees of freedom)
Always try first: Move optimization into control layer
Step 3. Implementation of optimal operation

## Slide 117: Optimization with PI-controller
max y
s.t. y ≤ ymax
u ≤ umax
Example: Drive as fast as possible to airport (u=power, y=speed, ymax = 120 km/h)
Optimal solution has two active constraint regions:
  y = ymax  speed limit
  u = umax  max power
Note: Positive gain from MV (u) to CV (y)
Solved with PI-controller
  ysp = ymax
  Anti-windup: I-action is off when u=umax
s.t. = subject to
y = CV = controlled variable
ysp = ymax
PI
Active constraint control using PI-controller

## Slide 118: The less obvious case: Unconstrained optimum
u: unconstrained MV
What to control? y=CV=?
J
uopt
Jopt

## Slide 119: Example: Optimal operation of runner
  Cost to be minimized, J=T
  One degree of freedom (u=power)
  What should we control?

## Slide 120: 1. Optimal operation of Sprinter
  100m. J=T
  Active constraint control:
    Maximum speed (”no thinking required”)
    CV = power (at max)

## Slide 121: 2. Optimal operation of Marathon runner
    40 km. J=T
    What should we control? CV=?
    Unconstrained optimum
u=power
J=T
uopt

## Slide 122
Any self-optimizing variable (to control at constant setpoint)?
    c1 = distance to leader of race
    c2 = speed
    c3 = heart rate
    c4 = level of lactate in muscles
Marathon runner (40 km)

## Slide 123: Conclusion Marathon runner
CV1 = heart rate
select one measurement
CV = heart rate is good “self-optimizing” variable
Simple and robust implementation
Disturbances are indirectly handled by keeping a constant heart rate
May have infrequent adjustment of setpoint (cs)
c=heart rate
J=T
copt

## Slide 124
Self-optimizing control
Self-optimizing control is when we can achieve an acceptable loss with constant setpoint values for the controlled variables

## Slide 125: The ideal “self-optimizing” variable is the gradient, Ju
c =  J/ u = Ju
  Keep gradient at zero for all disturbances (c = Ju=0)
Unconstrained degrees of freedom
u
cost J
Ju=0
Ju<0
Ju<0
uopt
Ju
0
Problem: Usually no measurement of gradient
Notes: 125

## Slide 126
H
Ideal: c = Ju
In practise, use available measurements: c = H y. Task: Select H!
Unconstrained degrees of freedom

## Slide 127: Combinations of measurements, c= Hy Nullspace method for H (Alstad): HF=0 where F=dyopt/dd
Proof. Appendix B in: Jäschke and Skogestad, ”NCO tracking and self-optimizing control in the context of real-time optimization”, Journal of Process Control, 1407-1416 (2011)
.
Unconstrained degrees of freedom

## Slide 128: Example. Nullspace Method for Marathon runner
u = power, d = slope [degrees]
y1 = hr [beat/min], y2 = v [m/s]
c = Hy, H = [h1 h2]]
F = dyopt/dd = [0.25 -0.2]’
HF = 0 -> h1 f1 + h2 f2 = 0.25 h1 – 0.2 h2 = 0
Choose h1 = 1 -> h2 = 0.25/0.2 = 1.25
Conclusion: c = hr + 1.25 v
Control c = constant -> hr increases when v decreases (OK uphill!)
Unconstrained degrees of freedom

## Slide 129
“Minimize” in Maximum gain rule
( maximize S1 G Juu-1/2 , G=HGy )
“Scaling” S1
“=0” in nullspace method (no noise)
With measurement noise
Exact local method for H
Notes: 129

## Slide 130: What variable c=Hy should we control? (self-optimizing variables)
BAD
Good
Good
The optimal value of c should be insensitive to disturbances
  Small HF = dcopt/dd
The value of c should be sensitive to the inputs (“maximum gain rule”)
  Large G = HGy = dc/du
  Equivalent: Want flat optimum
2
Unconstrained degrees of freedom in practice
1

## Slide 131: Example: CO2 refrigeration cycle
J = Ws (work supplied)
DOF = u (valve opening, z)
Main disturbances:
  d1 = TH
  d2 = TCs (setpoint)
  d3 = UAloss
What should we control?
pH

## Slide 132: CO2 refrigeration cycle
Step 1. One (remaining) degree of freedom (u=z)
Step 2. Objective function. J = Ws (compressor work)
Step 3. Optimize operation for disturbances (d1=TC, d2=TH, d3=UA)
    Optimum always unconstrained
Step 4. Implementation of optimal operation
    No good single measurements (all give large losses):
      ph, Th, z, …
    Nullspace method: Need to combine nu+nd=1+3=4 measurements to have zero disturbance loss
    Simpler: Try combining two measurements. Exact local method:
      c = h1 ph + h2 Th = ph + k Th; k = -8.53 bar/K
    Nonlinear evaluation of loss: OK!

## Slide 133: CO2 cycle: Maximum gain rule

## Slide 134: Refrigeration cycle: Proposed control structure
CV1= Room temperature
CV2= “temperature-corrected high CO2 pressure”
CV=Measurement combination

## Slide 135: Summary Step 3. What should we control (CV1)?
Selection of primary controlled variables c = CV1
  Control active constraints!
  Unconstrained variables: Control self-optimizing variables!
Self-optimizing control is an old idea (Morari et al., 1980):
“We want to find a function c of the process variables which when held constant, leads automatically to the optimal adjustments of the manipulated variables, and with it, the optimal operating conditions.”

## Slide 136: Self-optimizing control (SOC)
Challenges SOC:
Nonlinearity
Need new SOC variables for each active constraint region
  Similar to multiparametric optimization and lookup tables
Local approximation: c = Hy.
Need detailed steady-state model to find optimal H
  Nullspace method
  Exact local method
Must reoptimize for each expected disturbance
But calculations are offline

## Slide 137: 8. Classical Approach: Optimal operation using conventional advanced control
IFAC DYCOPS Pre-symposium workshop
Sigurd Skogestad

## Slide 138: Supervisory control layer
Alternative implementations:
Model predictive control (MPC)
Classical advanced control structures (PID, selectors, etc.)
RTO

## Slide 139: Model predictive control (MPC)
Can include constraints explicitly
If lack of DOF to meet control specifications:
  Conventional: Use weights
    (Partially) give up variables with small weights in objective function.
  Use two-stage MPC with constraint priority list:
    Stage 1. Check for steady-state feasibility and give up low-priority constraints if needed Stage 2. Solve conventional dynamic MPC

## Slide 140: Classical “Advanced control” structures
Cascade control (measure and control internal variable)
Feedforward control (measure disturbance, d)
    Including ratio control
Change in CV: Selectors (max,min)
Extra MV dynamically: Valve position control (=Input resetting =midranging)
Extra MV steady state: Split range control (+2 alternatives)
Multivariable control (MIMO)
    Single-loop control (decentralized)
    Decoupling
    MPC (model predictive control)
Extensively used in practice, but almost no academic work
CV = controlled variable (y)
MV = manipulated variable (u)

## Slide 141: Split range control: Donald Eckman (1945)

## Slide 142: Changing active contraints
Procedure for maintaining optimal operation when changing between active constraint regions
Step 1: Define all the constraints
Step 2: Identify relevant active constraint combinations and switches
Step 3: Propose a control structure for the nominal operating point.
Step 4: Propose switching schemes (see next)
Step 5: Design controllers for all cases (active constraint combinations)

## Slide 143: Switching between active constraints
1. Output to Output (CV - CV) switching (SIMO)
  Selector
2. Input to output (CV – MV) switching
  Do nothing if we follow the pairing rule: «Pair MV that saturates with CV that can be given up»
3. Input to input (MV – MV) switching (MISO)
  Split range control
  OR: Controllers with different setpoint value
  OR: Valve position control (= midranging control)

## Slide 144: Optimization with PI-controller
max y
s.t. y ≤ ymax
u ≤ umax
Example: Drive as fast as possible to airport (u=power, y=speed, ymax = 120 km/h)
Optimal solution has two active constraint regions:
  y = ymax  speed limit
  u = umax  max power
Note: Positive gain from MV (u) to CV (y)
Solved with PI-controller
  ysp = ymax
  Anti-windup: I-action is off when u=umax
s.t. = subject to
y = CV = controlled variable
ysp = ymax
PI
CV-MV switching

## Slide 145: Optimization with PI-controller
min u
s.t. y ≥ ymin
u ≥ umin
Example: Minimize heating cost (u=heating, y=temperature, ymin=20 °C)
Optimal solution has two active constraint regions:
  y = ymin  minimum temperature
  u = umin  heating off
Note: Positive gain from MV (u) to CV (y)
Solved with PI-controller
  ysp = ymin
  Anti-windup: I-action is off when u=umin
s.t. = subject to
y = CV = controlled variable
ysp = ymin
PI
CV-MV switching

## Slide 146: Optimization with PI-controller
The two examples:
Optimal operation: Switch between CV constraint and MV saturation
A simple PI-controller was possible because we followed the pairing rule:
  «Pair MV that saturates with CV that can be given up»
CV-MV switching

## Slide 147
MVs:
AC (expensive cooling)
CW (cooling water; cheap)
HW (hot water, quite cheap)
Electric heat, EH (expensive)
y=T
Split-range control (SRC): One CV (y). Two or more MVs (u1,u2)
Example: Room heating with 4 MVs
MV-MV switching

## Slide 148: Simulation PI-control: Setpoint changes temperature
MV-MV switching

## Slide 149
MVs:
AC (expensive cooling)
CW (cooling water; cheap)
HW (hot water, quite cheap)
Electric heat, EH (expensive)
y=T
Example: Room heating with 4 MVs
MV-MV switching
  Three Alternatives:
  Split range control (SP=22C)
  Controllers with different setpoint values (SP=24C, 23C, 22C, 21C)
  Valve position control (= midranging control) (Use always HW for SP=22C)

## Slide 150: Blending process with max selector
CV2
CV1
CV-CV switching
MV = Water feed (F2)
CV1 = Sugar concentration (Should be at SP=0.1 whenever feasible|)
CV2 = Impurity concentarion (Max. 0.001)
Disturbances: Variation in sugar feed (F1) and concentration of impurity in sugar
SUGAR with some impurity
WATER

## Slide 151
CV-CV switching

## Slide 152: Conclusion: Systematic procedure to avoid RTO-layer and even MPC-layer
Start “top-down” with economics (steady state):
Step 1: Define operational objectives and constraints
Step 2: Optimize steady-state operation
Step 3: Decide what to control (CVs)
  Step 3A: Identify active constraints = primary CV1.
  Step 3B: Remaining unconstrained DOFs: Self-optimizing CV1 (find H)
Step 4: Where do we set the throughput? TPM location
Then bottom-up (dynamics):
Step 5: Regulatory control
  Control variables to stop “drift” (sensitive temperatures, pressures, ....)
Finally: Make link between “top-down” and “bottom up”
Step 6: “Advanced/supervisory control”
    Control economic CVs: Active constraints and self-optimizing variables
    Look after variables in regulatory layer below (e.g., avoid saturation)
S. Skogestad, ``Control structure design for complete chemical plants'',
Computers and Chemical Engineering, 28 (1-2), 219-234 (2004).
CV1
CV2
Process
MVs
RTO

## Slide 153: Hierarchical Combination of different approaches
IFAC DYCOPS Pre-symposium workshop
Johannes Jäschke
Dinesh Krishnamoorthy

## Slide 154: Why not combine different approaches to give improved performance?!
Examples:
Combining model and data-based approaches
Combining online and offline methods
Some benefits
Faster rejection of known disturbances
Capability of handling unmodeled disturbances

## Slide 155: Standart RTO + MPC + self-optimizing control
  Self-optimizing Control
    Fast correction for known and modelled disturbances
  MPC:
    Predicting responses, and good constraint handling
  Standard RTO:
    Handling nonlinearity and large disturbances optimally
Idea: take the best from all worlds
Graciano et al. 2015, Journal of Process Control 34, 35–48

## Slide 156: Distillation Case Study
Separation of 3 components
RTO Problem
MPC
Setpoint tracking
  Standard (concentrations+temperature)
  Self-optimizing variable combinations
Constraint handling
  Enforce constraints as they become active

## Slide 157: Profit of combined approach
Disturbances are rejected also inbetween RTO updates.
--- standard MPC controlling
concentrations and 1 tray temp.
--- MPC Controlling SOC variables

## Slide 158: NCO tracking + self-optimizing control
Idea: take the best from both worlds
  Self-optimizing Control: Fast correction for known and modelled disturbances
  NCO tracking: use Plant gradient estimates to handle unmodeled disturbances

## Slide 159: Self-optimizing Control and NCO tracking
Self-optimizing control
Find a good output combination
Control to zero with favourite controller
NCO tracking idea
Measure gradient
Adjust input to make it zero
Plant gradient
NCO: Necessary conditions of Optimality

## Slide 160: Combination of self-optimizing control and NCO tracking
Fast time scale (lower layer):
  reject known (modelled) disturbances using self-optimizing control
Slow time scale (upper layer)
  reject unknown (unmodeled) disturbances in NCO tracking
Jäschke & Skogestad (2011)

## Slide 161
Self-optimizing and NCO tracking (sampling time 10 min)
Combined Self-optimizing and NCO tracking (sampling time 25 min)

## Slide 162
Similar approach: ESC/RTO + Self-optimizing control
Self-optimization control is always complementary
Can combine with
  Extremum-seeking control
  Traditional Static RTO
Straus. J, Krishnamoorthy, D., and Skogestad, S., 2018. On combining extremum seeking control and self-optimizing control. J. Proc. Control (In-Press).

## Slide 163
Case study: Ammonia Reactor
Objective: Maximize extent of reaction
Response to disturbance in inlet mass flow rate

## Slide 164: CONCLUSION: Why is traditional static RTO not commonly used? Some alternatives
Cost of developing and updating the model (costly offline model update)
 Fix: estimate plant gradients directly, like extremum-seeking - Machine learning (new)
2. Wrong value of model parameters and disturbances (slow online model update)
 Fix: DRTO, HRTO, self-optimizing control (fastest)
Not robust, including computational issues
 Fix: Feedback RTO, self-optimizing control
Frequent grade changes make steady-state optimization less relevant
 Fix: Dynamic RTO (DRTO) or EMPC
Dynamic limitations, including infeasibility due to (dynamic) constraint violation
 Fix: DRTO, EMPC (also HRTO ok!)
Incorrect model Structure
 Fix: Modifier adaptation

## Slide 165: Proposal : Combine RTO with other approaches
ESC / modifier adaptation layer: make RTO approach the real optimum .
SOC layer: make optimization faster, reduce wait time for model update and online optimization

## Slide 166: Conclusion
Data based approach
Plant gradient based method
Self-optimizing control
(in MPC/PID layer)
Real-time optimization
(SRTO/DRTO/HRTO)
Process
d
u
cs
Ju,s
J
y
Measurements
H
y
y
c
Slow (hour)
Extremely slow (days)
Fast (minute)
Model free
RTO:
Detailed model
(online)
SOC:
Detailed model
(offline)
Thank you !
Gradient estimator
Ju

## Slide 167
Next slide
Red box = bad, green box = good,
No box = neutral