## Slide 1: Absorption/Stripping
Gas-liquid separation processes
(Ch. 10)
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAAAAAAAAAAA

## Slide 2
Cooling
(condenser)
Distillation(Ch.11)
Absorption (Ch.10)
Stripping (Ch.10)
Heat
(reboiler)
Feed
A+B
Polluted
feed gas
B + A
Cleaned
Gas B
Polluted
feed liquid
Cleaned
Liquid C
A
B (heavy)
B
B
A
A
A
A
Absorbent
C
C+A
C+A
Stripping
gas B
B+A
Two key components (A+B)
One feed (normally)
Two pure products
Two sections
Heating and cooling
Boiling mixture
Three components
  Inert gas B (e.g., air)
  Inert liquid C (e.g., water)
  Solute A (e.g., CO2) goes from gas -> liquid
Two feeds
One pure product (at most)
One section
Non-boiling mixture
  so p and T can be set independently; see Exercise
Stripping: Reverse of absorption.
Solute A goes from liquid -> gas
COUNTER-CURRENT MULTISTAGE CONTACT OF GAS AND LIQUID
A
B

## Slide 3
«VANNVASK»
4 identical absorption columns
using pure water to absorb CO2
from N2/H2 in ammonia plant.
The only one in the world, as far as I know
Originally, the CO2 was used to make urea
but now the CO2 is the main supply of
«brus» in Norway and Sweden.
Sigurd Skogestad and Jan-Fredrik Arnulf (2013)
Designed about 1963 by Ingulf Skogestad, Norsk Hydro Engineering Office, Oslo.
Built at Herøya (Porsgrunn) about 1967 (Norsk Hydro ammonia plant NII, now Yara)

## Slide 4
6
5
4
3
2
1
9
8
7
0
10
Abs.
Tower
(4 towers,
Each
D=3.3m
h=35m
77 trays)
24 bar
10 C
Flash
5.5 bar
10 C
Pure water from lake, 2000 m3/h
Pump
Turbine
CO2 product
Water to sea
Synthesis gas, 6700 kmol/h
17% CO2, 35C
Gas to
ammonia
Plant
0,3% CO2
Water recycle, 6000 m3/h
Air
220 000 Nm3/h
Blower
Air
with CO2
0.39% CO2
1.1 bar
10 C
Revidert SiS. 24. jan. 2017
EXAM, Dec. 2016

## Slide 5: Remove water from natural gas

## Slide 6
Example: CO2 capture from coal power plant (A=CO2)
Partial
A=CO2
B=air
C=water/amine
A=CO2
B=steam (generated by reboiler)
C=water/amine

## Slide 7: Absorption/stripping
Two solution approaches
Equilibrium-stage model (Ch. 10.3). Find N
  Similar to distillation
  (A) Graphical: McCabe-Thiele (any VLE)
  (B) Analytical: Kremser (VLE: Assume dilute solution. 1) Henry’s law, y = mx, +2) assume L/V constant)
Mass transfer model, (Ch. 10.4+10.6).
  Find A=aSz (A=interfacial area)
  Similar to heat transfer in heat exchanger
    (A) Graphical: Must combine with integration
    (B) Analytical (Henry’s law): Log-mean driving, (y-y*)LM

## Slide 8: Graphical method (McCabe-Thiele) for absorption/stripping
Equilibrium line usually straight line because of dilute solution
Operating line goes through end points
  These point are not on the diagonal*
  Usually straight operating line because of dilute mixture
*Note: For distillation the operating lines go through (xD,xD) and (xB,xB), which are on the diagonal.
  Reason: Reflux/boilup generates “feed stream” with same composition as product.

## Slide 9: Flows [mol/s]
Flows generally vary through the column
L = L’/(1-x)
V = V’/(1-y)
x, y = mole fractions of component being transferred (A)
L’ = inert liquid molar flow (C)
V’ = inert vapor molar flow (B)
For dilute mixtures we can assume (1-x)=1 and (1-y)=1 so L and V are constant through the column.

## Slide 10
m=2.53, L/V=3
L=90 kmol/h, V=30 kmol/h

## Slide 11
From last time:

## Slide 12
m=2.53, L/V=3
L=90 kmol/h, V=30 kmol/h
Solution: Need N=5.2 (approx.)
(xN, yN+1): Bottom end
(x0, y1): Top end

## Slide 13: Minimum flows Absorption: Lmin Stripping: Vmin
Absorption: Pinch (equilibrium) in bottom where vapor feed enters
Stripping: Pinch (equilibrium) in top where liquid feed enters
Corresponds to N=1

## Slide 14: Lmin: Back to example
x’N = x*N+1 = yN+1/m = 0.01/2.53 = 0.004
From figure: Lmin/V = (yN+1 – y1)/(x*N+1-x0) = (0.01-0.001)/(0.004-0)= 2.277
So: Lmin = 30*2.277 = 68.3 kmol/h
Operating line with Lmin
* = in equlibrium with the other phase
Example: x*N+1 is (imaginary) liquid composition in equlibrium with y*N+1

## Slide 15: Lmin: «Alternative» derivation
From overall mass balance (assuming constant flows)
  V yN+1 + L x0 = V y1 + L xN
Assume equlibrium in bottom (pinch)
  xN = x*N+1 = yN+1/m = 0.0040
Get min. reflux. Lmin/V = (yN+1 – y1)/(x*N+1-x0)

## Slide 16: Minimum stages, Nmin
No such thing for absorption/stripping (Nmin=0)
Example: 1 stage is OK if we increase flows enough
  Absorption: increase L enough
  Stripping: increase V enough

## Slide 17: N=1: Back to example
From figure: L/V = (yN+1 – y1)/(x*1-x0) = (0.01-0.001)/(0.0004-0)= 22.77
So: L = 30*22.77 = 683 kmol/h
Operating line with N=1
x*1 = y1/m = 0.001/2.53 = 0.0004

## Slide 18: Kremser equations
Analytical solution for case with straight equilibrium line (y=mx) and L/V constant (dilute mixtures)
A = (L/V)/m – absorption factor = ratio of slopes for operating and equilibrium lines
  Absorption: want A large
  Stripping: Want A small
y*0 = mx0
y*N = mxN
L
V
L
V
= in equilibrium with other phase
(could be imaginary composition, like y*0)
(next page)

## Slide 19
*

## Slide 21: Example 1: A fun absorption problem
Dear Absorption and distillation experts: Can you solve this? This problem is based on a true story. My father, Ingulf Skogestad, got his degree as a chemical engineer at NTH in Trondheim in 1948. It was difficult to find good process jobs in Norway at that time, so his career got a boost when he during 1956-61 worked at two ammonia plants that ICI operated in South Africa.
This is a story from Modderfontein near Johannesburg in 1959 where they had a problem of not reaching the gas spec. in an absorption tower. They build an identical tower no. 2 (in series) but still they could not reach the spec. My father found a solution that worked: He took the absorbent (liquid) from tower 2 and used it in tower 1 (and left tower 2 as a spare). This was at the time explained by the fact that there was too little liquid in tower 1 to get proper wetting of the packing, but I think it may have been a more fundamental mass balance problem.
To illustrate this I have made the following problem: A gas stream of 1 mol/s has 4 mol% of component A, and it should be reduced to 0.1% in an absorption tower with use of 6 mol/s pure water. However, in spite of the tower being very tall, the fraction of A in the gas product is too high (about 1.6% A). To reduce the concentration of A, an identical tower 2 is build, where the exit gas from tower 1 (with 1.6% A) is treated with 6 mol/s pure water. However, one still is not able to reach the desired 0.1% A. Data: Henry's law for component A: y = mx, where m = H/p = 10 (p is the column pressure, which is 1 bar). (a) Make a flowsheet for the two alternatives. (b) Can it be correct that one achieves 1.6% A in tower 1? (c) What is the concentration of A in the gas leaving tower 2? (d) An engineer always finds a solution! In this case it is to use all the water (12 mol/s) in tower 1 (and leave tower 2 as a spare). Can you explain why this works, and find the exit gas concentration of A in this case.
Minimum flows

## Slide 22
Original design:
(One tower, 6 mol/s water)
Polluted gas
V=1 mol/s
y1 = 0.04
Polluted gas
V=1 mol/s
y1 = 0.04
Cleaned gas
Desired: y2 = 0.001
Actual: y2=0.016
(b) Vy2 = Vy1 – Lx1) y2=0.016
L=6 mol/s
x2=0 (pure water)
L=6 mol/s
x2=0
L=6 mol/s
x2=0
Cleaned gas
Desired: y2 = 0.001
(c) Actual: y2=0.0064
V’y’2 = V’y’1 – L’x’1) y’2=0.0064
2. New design
(Two towers in series,
total 12 mol/s water)
3. Final design**
(One tower, 12 mol/s water)
L=12 mol/s
x2=0 (pure water)
Polluted gas
V=1 mol/s
y1 = 0.04
Cleaned gas
Desired: y2 = 0.0012
Actual: y2<0.001
(d) Not enough data to find exact y
(need N or similar)
Btm:
Close to equilibrium (pinch):
x1=x1*=y1/m=0.04/10=0.004.
(L/V)min= (0.04-0.001)/0.004=9.75
Pinch:
x'1=x’1*=0.016/10=0.0016
y’1=y2=0.016
end 2
end 1
**If liquid load too large:
Can split the gas and have
two towers in parallel.
Each with half L and V.

## Slide 23: Example 2 (Problem 2, exam 2004)
PROBLEM 2. STRIPPING.
Water from an oil installation contains 8 mg benzene per liter water. It should be reduced to 0.4 mg benzene per liter by stripping with air at 2 atm.
(a) Find the minimum amount of air (m3 air/m3 water). How many equilibrium stages does this require?
SOLUTION. General approach:
Convert everything to molar + (Find product streams from mass balance)
Minimum flows: This is with infinite no. of stages and it occurs when we have “pinch”
  For absorption/stripping: “Pinch” at one end -> product and feed in equilibrium!
V (air)
L (water+ benzene)
Assume: L and V constant through column (dilute-> x and y small)
+ Assume T=300K (not given!) + assume ideal gas
(i) Conversion to molar: “8 mg benzene per liter water”.
nb = 8 mg benzene = 8e-3 g / 78 g/mol = 1.026e-4 mol
nw= 1 liter water = 1 kg water = 1000g/ 18 g/mol = 55.55 mol
x0 = nb/(nb+nx) = 1.846 e-6 = 1.846 ppm
Similar: xN = x0*0.4/8 = 0.05 x0 = 9.231 e-8 = 0.092 ppm
Infinite number of stages: y1 and x0 are in equilibrium -> y1 = (H/p) x0 = (383.5 bar/2bar)*1.846e-6 = 3.54e-4 = 354 ppm
(ii) Can now find minimum air flow from overall material balance:
Lx0 + VyN+1 = LxN + Vy1
Or L(x0-xN) = V (y1-yN+1)
Or V = L(x0-xN)/(y1-yN+1) = L (1.846-0.092)/(354-0) = 0.00495 L [mol/s]
Water: Given L = 1 m3 = 1000 kg = 55.55 kmol
Air: Get V = 0.00495 L = 0.275 kmol = 275 mol = 275 (RT/p) [m3] = 275*8.31*300/2e5 [m3] = 3.43 m3 (gas)
eq.
Minimum flows

## Slide 24: Diffusion (Two-film theory)
See lecture no. 3 from Jana
Mass transfer based on bulk compositiums
NA = Ky (y-y*) = Kx (x-x*) [mol/s m2]
Ky = m Kx
Assume dilute mixture, so that drift of film can be neglected:
Ky = K’y
To find overall mass transfer coefficient: Add resistances: 1/Ky = 1/ky + m/kx

## Slide 26: Mass transfer approach
Two-film mass transfer model
Bulk phases not in equilibrium
Dilute mixtures (1-x ¼1)
  Henry’s law: y*i = m xi
  Constant (molar) flows: L ¼ L’ (inert)
Mass transfer (Non-equilibrium) model
Get differential equation (dnA/dz=…) instead of difference equations:
    Mass transfer: NA = Ky (y – y*) [mol A/s, m2]
    Mass balance over dz: dnA = Vdy = NA dA, where dA = aSdz
    Combine: dz = V dy / Ky a S (y-y*)
      Packing height (integrate):
      Integrate expression for NOG numerically (computer) or graphically (exercise)
      For dilute mixtures (Analytical Log-mean approximation):
HOG [m]
= hight of
transfer unit
NOG [-]
= number of
transfer units
NOG =

## Slide 27: Proof of expression for NOG
y-y* is the difference between the operating and equilibrium lines and for dilute mixtures it changes linearly with x (and with y) so write1:
  y-y* = ky + b
Book (p. 671) says that this «can be integrated» to get the desired result, but skips the details. Here is a proof.
Integral of 1/(y-y*)=1/(ky+b) is ln(ky+b)/k = ln(y-y*)/k
Integrate this from end 2 to end 1, get
  NOG = ln [(y-y*)1/(y-y*)2] * 1/k
Now the «trick» comes. Note that k is the slope of (y-y*) as a function of y. So using the two ends 1 and 2, we have
  k = [(y-y*)1-(y-y*)2] / [y1 – y2]
  QED
  1. Comment: By writing y=(L/V)x+a and y*=mx, we have that y-y*=(L/V - m)x + a, and by using x = (y-a)/(L/V) we find that k = (L/V – m)/(L/V) = 1 – 1/A where A=(L/V)/m

## Slide 28: Absorption/stripping in packed towers. Useful log-mean formula for dilute mixtures
2
1
z
y
y*=mx

## Slide 29: Multistage separation with given products: Minimum number of stages
There is no “minimum number of stages” in absorption/stripping
Can have N -> 0 if we have very large flow (of solvent or stripping gas).
Note: Purities of incoming streams (column ends) are fixed, and this limits product purities, independent of the number of stages.
Distillation is different: Here we “recycle” at the column ends and can achieve any product purity by increasing the number of stages.
  Fenske: Nmin = lnS/ln®

## Slide 30: Multistage separation with given products: Minimum flows (Lmin, Vmin)
Absorption/stripping: minimum solvent/stripping gas
Obtained with infinite large column (infinite no. of stages)
General: Occurs when we have “pinch” somewhere
  No change in composition between stages
  = Crossing of equilibrium and operating line
  = Compositions between stages in equilibrium
Absorption/stripping: usually occurs at column end
    -> one product is in equilibrium with its feed

## Slide 31: 10.6C Pressure drop and flooding in packed columns
To find column diameter and pressure drop:
Obtain packing factor Fp (from Table)
Find flooding pressure drop
Find corresponding flooding gas velocity (using pressure drop correlation in Figure)
  Typical: vflood is about 6.6 ft/s = 2 m/s
Choose diameter such that gas velocity is about half of this
  Typical: Design for v = 1 m/s
Find pressure drop in column (from pressure drop correlation in Figure)

## Slide 32
Table 10.6-1.
Packing factors Fp

## Slide 33
Pressure drop correlations

## Slide 34: 11.5F Flooding velocity and Diameter of tray towers
To find column diameter and pressure drop:
Obtain tray factor Kv [ft/s] (from Figure)
Find entrainment gas velocity from eq. 11.5-14 (occurs just before flooding). Fair correlation:
Choose diameter so that gas velocity is about v = 0.7 vmax
Pressure drop: Usually much larger than in packed columns, because of pressure drop for gas to pass through liquid on trays

## Slide 35
6’’ = 6 inches = 18 cm

## Slide 36: Summary: Absorption/Stripping
Single section
Notation varies…
Dilute mixtures:
  1-x ¼1
  Henry’s law: pi = H xi
    Using pi = yi p gives
    yi = (H/p) xi = m xi
  Constant (molar) flows: L ¼ L’ (inert)
Modelling. Two approaches
  Equilibrium stage (as for distillation, but simpler)
    (A) Graphical: McCabe Thiele for nonideal VLE
    (B) Analytical for dilute mixtures: Kremser formulas. A = (L/V)/m
  Mass transfer (Non-equilibrium) models

## Slide 37: Summary countercurrent vapor-liquid separation
 | Stage model (Tray column) | Differential model (Packed column)
Equilibrium (between liquid and vapor bulk phases) | Eq. stage. (Most common model in practice!) McCabe-Thiele Dilute: Fenske, Kremser | (Not possible with differential model*) (But one can use eq. stage + HETP!)
Non-equilibrium | (Not covered in this course) Non-equilibrium between bulk phases is used sometimes. May use two-film theory on stages | Most common is two-film approach. Nondilute: Numerical integration Dilute mixtures: log-mean formula.
*Would give column with height=0